## Slide 1: Lecture 12
Analog to Digital Converters

## Slide 2: Analog to Digital Converters
What is an ADC?
Output vs. input
Input range
Single-ended vs. differential inputs
Output coding: unipolar vs. bipolar
Recap: C8051F020 analog peripherals
12-bit ADC (ADC0)
  Starting ADC0 conversions
  Data word conversion map (12-bit)
  Programming ADC0
  Detecting ADC0 end-of-conversion
  SAR0 conversion clock frequency
  ADC0 programming example—polling method
  ADC0 programming example—interrupt method
Appendix: 8-bit ADC (ADC1)
Notes: <number>
<footer>
<header>
<date/time>
In this lecture we will learn all about programming the ADCs.

## Slide 3: What is an ADC?
ADC is the acronym for analog-to-digital converter
An ADC takes an analog voltage at its input and produces a digital number representing that voltage at its output

## Slide 4: Output vs. Input
The output of an ADC is different from the input in two distinct ways:
  The input signal to the ADC is a continuous voltage, while the ADC output has been quantized to discrete steps that are represented as digital codes
  The input signal is continuous in time, while the output is a series of discrete-time points
Notes: The output of an ADC is an approximation of the analog input. The accuracy of this approximation depends both on the analog precision of the ADC and the speed at which it can sample the input.

## Slide 5: ADC—Input Range
An ADC’s input range is defined by the reference voltage (VREF) provided to the ADC
The power supplies to the ADC are also important in determining the absolute input voltage
  In most ADC architectures, input voltages outside the supply rails cannot be measured and may cause damage to the device
Notes: The reference voltage defines one, sometimes both end points of the transfer function, depending on the type of ADC.
Silicon Labs does sell one MCU family (the C8051F04x) which incorporates a high-voltage difference amplifier in front of the ADC. The HVDA can accept absolute voltage inputs between +/-60 volts without damage.

## Slide 6: ADC—Single-Ended
A “single-ended” ADC is one where a single input voltage is measured with respect to ground (AIN–GND).
  Most single-ended ADCs have an input range from 0V to VREF
  Common Problem: Input circuitry’s maximum output higher than VREF
Notes: If the ADC input voltage is above VREF, but below the supply voltage for the ADC, the device will not be damaged, but the ADC output will max out and saturate at full-scale.

## Slide 7: ADC—Single-Ended Supply Measurement
One example of a single-ended voltage measurement is monitoring the supply to the system—the supply is divided down to within the input range of the ADC using a resistive divider

## Slide 8: ADC—Differential
For a differential ADC, the difference in voltage between two pins is measured (AIN+ - AIN-)
  The input range of a differential converter is –VREF to +VREF, or twice the range of a single-ended converter
  Common Problem: Input circuitry designed to go below ground when supply to ADC is only positive
Notes: The absolute maximum voltage range (with respect to GND) on the inputs to the ADCs is between the supply rails, even though the ADC may measure a negative value between the two inputs AIN+ and AIN-.

## Slide 9: ADC—Differential
A “negative” differential measurement does not require a negative input voltage
If the difference between AIN+ and AIN- is negative, a negative output will be produced
  If AIN+ = 1 V and AIN- = 2 V, the input to the ADC is
  (AIN+ - AIN-) = (1 V – 2 V) = -1 V

## Slide 10: ADC—Differential Bridge Measurement
An example of a differential input signal is a bridge measurement (such as a load cell)
The voltage of interest is the difference across the bridge
Notes: A bridge circuit is made up of resistors, some of which vary with change in a physical parameter. In a load cell for example, the variable elements are sensitive to pressure. When these elements change, the output of the resistive dividers also change.

## Slide 11: ADC—Output Coding
The output code range of an ADC is 2N, where N is the number of bits in the output word
The digital output from an ADC represents the voltage present at the input, as a fraction of the reference voltage. With a single-ended converter whose input range is 0 V to VREF
  Output = (VIN / VREF) x 2N; N = number of bits in output word
To calculate the input voltage from the output code:
  VIN = VREF x (Output / 2N); N = number of bits in output word
The term “LSB” is commonly used to refer to the amount of input voltage required to produce a single-code change at the output
  One LSB = input voltage range/output code range
  Example: For a single-ended 12-bit ADC using a 2.4 V reference, one LSB = (VREF / 212) = (2.4 V / 4096) = 0.59 mV
Notes: We are going to use the Output equation a number of times later in this section. Pay special attention to this equation.
The size of an LSB is derived from the “Vin” equation. By setting the output to a value of 1, Vin becomes the LSB size.

## Slide 12: ADC—Unipolar Output Coding
Unipolar output coding is used when the input signal to the ADC is positive
For a single-ended converter, output coding is normally unipolar
Unsigned binary encoding is used to represent unipolar output
Input Voltage | Output Code (12-bit)
>= VREF | 4095 (0x0FFF)*
VREF – 1 LSB | 4095 (0x0FFF)
½ VREF | 2048 (0x0800)
¼ VREF | 1024 (0x0400)
0 V | 0 (0x0000)
* Output of ADC is saturated | 
Notes: Note that voltages above VREF will saturate the output at full scale.

## Slide 13: ADC—Bipolar Output Coding
Bipolar output coding is used when the input to the converter can be positive or negative, as with a differential converter
For a differential converter, the input range is doubled, which also doubles the size of the LSB
2’s-complement binary encoding is typically used to represent bipolar output
Input Voltage | Output Code (12-bit, sign extended)
>= VREF | 2047 (0x07FF)*
VREF – 1 LSB | 2047 (0x07FF)
½ VREF | 1024 (0x0400)
0 V | 0 (0x0000)
- ½ VREF | -1024 (0xFC00)
-VREF | -2048 (0xF800)
< -VREF | -2048 (0xF800)*
*Output of ADC is saturated | 
Notes: Voltages above or below the limits will saturate the output to full scale.

## Slide 14: Recap—C8051F020 Analog Peripherals
C8051F020 contains the following analog peripherals:
  One 8-bit and one 12-bit analog-to-digital converters (ADC)
  Two 12-bit digital-to-analog converters (DAC)
  Programmable gain amplifiers (PGAs)
  Analog multiplexer (8-channel and 9-channel)
  Two analog comparators
  Precision voltage reference
  Temperature sensor
Notes: <number>
<footer>
<header>
<date/time>
C8051F020 is many miles ahead of its competitors in terms of on-board analog resources. There are two very accurate and fast multi-channel ADCs with programmable gain amplifiers, two 12-bit DACs, two analog comparators with programmable hysteresis, a high-precision voltage generator and on-chip temperature sensor.

## Slide 15: 12-Bit ADC (ADC0)
Notes: <number>
<footer>
<header>
<date/time>
This diagram shows the various blocks and SFRs of the 12-Bit ADC module which is referred to as ADC0. It operates at 100 ksps (kilo samples per second) conversion rate. There are 9 inputs to the multiplexer – 8 external and one from the on-chip temperature sensor. C8051F020 has dedicated pins available for the 8 inputs. The inputs can be configured in single ended or differential modes. The ADC conversion can be started in four different ways. The converted digital value is available in the registers ADC0H (high byte) and ADC0L (low byte).
Two registers (ADC0GT and ADC0LT) can be programmed to set higher and lower threshold values; when the measured analog voltage is outside the window limits set by the threshold registers, an interrupt (AD0WINT) can be generated.

## Slide 16: 12-Bit ADC (ADC0)
The ADC0 subsystem consists of:
  9-channel, configurable analog multiplexer (AMUX0)
    8 channels for external input
      Single-ended inputs
      Differential input pairs
    9th channel for on-chip temperature measurement
  Programmable gain amplifier (PGA0)
    Default gain is 1
    Gain can be programmed to be 0.5, 1, 2, 4, 8 or 16
  12-bit Successive approximation register (SAR) ADC
ADC0 is enabled by setting AD0EN (ADC0CN.7) to 1
Notes: <number>
<footer>
<header>
<date/time>
  The Programmable gain amplifier (PGA0) has a default gain of 1. The gain can be programmed to be 0.5, 1, 2, 4, 8 or 16 by programming the AMP0GN2-0 bits in the ADC0CF (ADC0 Configuration) Register. This register will be discussed later in another slide. The entire ADC0 is enabled/disabled by setting/resetting the AD0EN (ADC0CN.7) bit.

## Slide 17: Starting ADC0 Conversions
Conversions can be started in four different ways (depending on the AD0CM1 and AD0CM0 bits in ADC0CN register)
  Software command (writing 1 to AD0BUSY)
  Overflow of timer 2
  Overflow of timer 3
  External signal input (rising edge of CNVSTR)
The AD0BUSY bit remains set to 1 during conversion and restored to 0 when the conversion is complete
The falling edge of AD0BUSY triggers an interrupt (when enabled) and sets the AD0INT interrupt flag (ADC0CN.5)
If ADC0 end-of-conversion interrupt (EIE2.1) is enabled, then an interrupt will be generated when AD0INT is set and the appropriate ADC0 ISR will be executed
Notes: <number>
<footer>
<header>
<date/time>
ADC0 conversions can be started in four different ways - Software command (i.e. by writing 1 to AD0BUSY bit), Overflow of Timer 2, Overflow of Timer 3, External signal input (rising edge of CNVSTR). The conversion start method is selected by programming the AD0CM1 and AD0CM0 bits in ADC0CN register.
While the conversion is in progress, the AD0BUSY bit remains set to 1. It is restored to 0 when the conversion is complete. On the falling edge of AD0BUSY, the AD0INT interrupt flag (ADC0CN.5) is set. In a polling method, one can check the status of AD0INT flag to detect the completion of conversion.
If ADC0 End-of-Conversion Interrupt (EIE2.1) is enabled, then an interrupt will be generated and the corresponding ADC0 ISR will also be executed.

## Slide 18: Data Word Conversion Map (12-bit)
Converted data is stored in the ADC0H and ADC0L registers and can be either left- or right-justified in the register pair depending on the programmed state of the AD0LJST (ADC0CN.0) bit
  ADC0H[3:0]:ADC0L[7:0], if AD0LJST = 0
  (ADC0H[7:4] will be 0000b)
  ADC0H[7:0]:ADC0L[7:4], if AD0LJST = 1
  (ADC0L[3:0] = 0000b)
The mapping of the ADC0 analog inputs to the ADC0 data word registers is given by:
where n=12 for single-ended and n=11 for differential inputs
ADC0H
ADC0L
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
Notes: <number>
<footer>
<header>
<date/time>
The converted digital data in the ADC0H and ADC0L registers put together can be left or right justified. This is achieved by programming the AD0LJST (ADC0CN.0) bit.
The converted digital value is a function of the input analog voltage, the reference voltage used, the gain of the PGA (Programmable Gain Amplifier) and the whether the inputs are configured in single-ended or differential mode.

## Slide 19: Data Word Conversion Map (12-bit)
Suppose AIN0 is used as the input in single-ended mode (AMX0CF=00H and AMXSL=00H) and gain is set to 1
AIN0 – AGND (Volts) | ADC0H:ADC0L (AD0LJST=0) Right Justified | ADC0H:ADC0L (AD0LJST=1) Left Justified
 | 0FFFH | FFF0H
 | 0800H | 8000H
 | 07FFH | 7FF0H
0 | 0000H | 0000H
Notes: <number>
<footer>
<header>
<date/time>
For single-ended inputs and gain set to 1, the input voltage range is from 0 to (VREF*4095/4096).

## Slide 20: Programming ADC0
ADC0 can be programmed through the following sequence
  Step 1: configure the voltage reference (REF0CN)
  Step 2: set the SAR0 conversion clock frequency and PGA0 gain (ADC0CF)
  Step 3: configure the multiplexer input channels (AMX0CF)
  Step 4: select the desired multiplexer input channel (AMX0SL)
  Step 5: set the appropriate control bits and start-of-conversion mode and turn on ADC0 (ADC0CN)
Notes: <number>
<footer>
<header>
<date/time>
The various SFRs used to control and manage the ADC0 are REF0CN, ADC0CF, AMX0CF, AMX0SL and ADC0CN. The programming sequence for ADC0 are enumerated in this slide.

## Slide 21: Configuring the ADC0 Voltage Reference
2.4V Output of Internal VREF
Notes: <number>
<footer>
<header>
<date/time>
We have seen this slide once before, in Lecture 2. This shows the various ways of providing the reference voltage to the ADCs and DACs.
For ADC0, the voltage reference could be from VREF0 or the DAC0 output (which is itself programmable). This is achieved by programming the AD0VRS (REF0CN.4) bit. VREF0 may be connected to VREF (i.e. the internal voltage generator) or an external voltage reference.

## Slide 22: Reference Control Register—REF0CN
Bit | Symbol | Description
7-5 | - | Unused. Read=000b; Write=Don’t care.
4 | AD0VRS | ADC0 Voltage Reference Select 0: ADC0 voltage reference from VREF0 pin. 1: ADC0 voltage reference from DAC0 output.
3 | AD1VRS | ADC1 Voltage Reference Select 0: ADC1 voltage reference from VREF1 pin. 1: ADC1 voltage reference from AV+
2 | TEMPE | Temperature Sensor Enable Bit 0: Internal Temperature Sensor Off. 1: Internal Temperature Sensor On.
1 | BIASE | ADC/DAC Bias Generator Enable Bit. (Must be ‘1’ if using ADC or DAC) 0: Internal Bias Generator Off. 1: Internal Bias Generator On.
0 | REFBE | Internal Reference Buffer Enable Bit. 0: Internal Reference Buffer Off. 1: Internal Reference Buffer On. Internal voltage reference is driven on the VREF pin.
Notes: <number>
<footer>
<header>
<date/time>
If ADC or DAC is used, the BIASE bit (REF0CN.1) must be set to 1 (i.e. the Internal Bias Generator must be ON). The temperature sensor is enabled by setting the TEMPE bit (REF0CN.2).

## Slide 23: ADC0CF—ADC0 Configuration Register
Bit | Symbol | Description
7-3 | AD0SC4-0 | ADC0 SAR0 Conversion Clock frequency Bits SAR0 Conversion clock is derived from system clock by the following equation, where AD0SC refers to the 5-bit value in AD0SC4-0 and CLKSAR0 refers to the desired ADC0 SAR conversion clock frequency.
2-0 | AMP0GN2-0 | ADC0 Internal Amplifier Gain (PGA) 000: Gain = 1 001: Gain = 2 010: Gain = 4 011: Gain = 8 10x: Gain = 16 11x: Gain = 0.5
Notes: <number>
<footer>
<header>
<date/time>
This table shows the various bits of ADC0CF (ADC0 Configuration) Register that must be programmed to (a) set the gain of the PGA (b) set the SAR0 Conversion Clock Frequency.
(SAR is Successive Approximation Register)

## Slide 24: SAR0 Conversion Clock Frequency
The conversion clock has a maximum frequency of 2.5 MHz
The conversion clock frequency is calculated using the following equation:
If the System Clock Frequency is 16 MHz and AD0SC4-0 is set to 10000b, then the SAR0 conversion frequency is 16MHz/17 = 941.176 KHz
If the value loaded in ADC0CF is 10000000, then the SAR0 conversion frequency will be 941 KHz approximately and the PGA0 gain will be set to 1
Notes: <number>
<footer>
<header>
<date/time>
For ADC0, the SAR conversion clock has a maximum frequency of 2.5 MHz. The SAR conversion clock frequency depends on the System Clock Frequency and the value of the bits AD0SC4-0 in the ADC0CF (ADC0 Configuration) register.

## Slide 25: AMX0CF—AMUX0 Configuration Register
Bit | Symbol | Description
7-4 | - | UNUSED. Read=0000, Write=don’t care
3 | AIN67IC | AIN6, AIN7 Input Pair Configuration Bit 0: AIN6 and AIN7 are independent single-ended inputs 1: AIN6, AIN7 are (respectively) +,- differential input pair
2 | AIN45IC | AIN4, AIN5 Input Pair Configuration Bit 0: AIN4 and AIN5 are independent single-ended inputs 1: AIN4, AIN5 are (respectively) +,- differential input pair
1 | AIN23IC | AIN2, AIN3 Input Pair Configuration Bit 0: AIN2 and AIN3 are independent single-ended inputs 1: AIN2, AIN3 are (respectively) +,- differential input pair
0 | AIN01IC | AIN0, AIN1 Input Pair Configuration Bit 0: AIN0 and AIN1 are independent single-ended inputs 1: AIN0, AIN1 are (respectively) +,- differential input pair
Notes: <number>
<footer>
<header>
<date/time>
Bits 3-0 of AMX0CF (AMUX0 Configuration) Register are used to set the mode of the analog inputs – either single-ended or different input pair. By default, the inputs are set in single-ended mode.

## Slide 26: AMX0SL—AMUX0 Channel Selection Register
Bit | Symbol | Description
7-4 | - | UNUSED. Read=0000, Write=don’t care
3-0 | AMX0AD3-0 | AMX0 Address Bits 0000-1111: ADC Inputs selected according to channel selection table on next slide.
Notes: <number>
<footer>
<header>
<date/time>
The AMX0AD3-0 bits in the AMX0SL (AMUX0 Channel Selection) Register are used to select the input channel.

## Slide 27: AMUX0 Channel Selection—AMX0SL SFR
Notes: <number>
<footer>
<header>
<date/time>
This table shows the values of the AMX0CF (Bits 3-0) and AMX0AD3-0 for various combinations of input channels and modes (single-ended or differential pair)

## Slide 28: ADC0CN—ADC0 Control Register
Notes: <number>
<footer>
<header>
<date/time>
The ADC0CN (ADC0 Control) Register is programmed to enable/disable ADC0, left/right justify the converted digital data, select the start of conversion mode and tracking mode. It also has the flag (AD0INT) to monitor the end-of-conversion. AD0BUSY flag can be set to start a conversion and it remains set till the conversion is complete.

## Slide 29: Detecting ADC0 End-of-Conversion
Polling Method
  AD0INT bit (ADC0CN.5) may be polled to determine when a conversion has completed
  Once the bit is set, read the ADC0 data
Interrupt Method:
  If ADC0 End-of-Conversion Interrupt (EIE2.1) and global interrupts are enabled, then an interrupt will be generated and the appropriate ADC0 ISR will be executed
  Inside the ADC0 ISR, read the ADC0 data
Notes: <number>
<footer>
<header>
<date/time>
There are two ways to detect the end-of-conversion – Polling method by monitoring the AD0INT bit (ADC0CN.5), and Interrupt method by enabling the EIE2.1 bit.

## Slide 30: ADC0 Programming Example—Polling Method
void Init_ADC0(void)
{
REF0CN = 0x07; //--Enable internal bias generator and
// internal reference buffer
// Select ADC0 reference from VREF0 pin
// Internal Temperature Sensor ON
ADC0CF = 0x81; //--SAR0 conversion clock=941KHz approx
// Gain=2
AMX0SL = 0x08; //--Select Temp Sensor
ADC0CN = 0x80; //--Enable ADC0, Continuous Tracking
// Mode Conversion initiated on write to
// AD0BUSY; ADC0 data is right justified.
}
void main (void)
{
Device_Init (); // Init device peripherals
AD0BUSY = 1; // Start ADC conversion
while (!AD0INT); // Wait till conversion is complete
ADC0_Value = ADC0; // Store ADC result in variable
AD0INT = 0; // Clear AD0INT flag
while (1); // Spin forever
}
Notes: <number>
<footer>
<header>
<date/time>
Sample code for detecting end-of-conversion using polling method. Timer 3 overflow starts the conversion. Inside the Timer 3 ISR, we poll the AD0INT bit and wait for it to be set to 1 before reading the ADC0 register.

## Slide 31: ADC0 Programming Example—Polling Method
The timer 3 overflow is used to initiate ADC0 conversion
Timer 3 interrupt is also enabled (not shown in the code)
Timer 3 ISR is executed as soon at the ADC conversion starts
Within the timer 3 ISR, we first reset the TF3 (timer 3 overflow flag) and then poll the AD0INT flag, waiting for it to set to 1
The AD0INT flag is set when the ADC conversion is complete
We then read the ADC conversion value from the register ADC0 and load it into the variable ADC0_reading
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32: ADC0 Programming Example-Interrupt Method
We could also use the ADC0 interrupt, which can be enabled by setting EADC0 (EIE2.1) and enabling global interrupts
The ISR for ADC0 will be called each time the conversion is completed
Inside the ISR, we simply need to:
  Read the ADC0 register
  Store the value in a variable
  Clear the AD0INT flag
Notes: <number>
<footer>
<header>
<date/time>

## Slide 33: ADC0 Programming Example—Interrupt Method
void Init_ADC0(void)
{
REF0CN = 0x07; //-- Enable internal bias generator and
// internal reference buffer
// Select ADC0 reference from VREF0 pin
// Internal Temperature Sensor ON
ADC0CF = 0x81; //-- SAR0 conversion clock=941KHz approx
// Gain=2
AMX0SL = 0x08; //-- Select Temp Sensor
ADC0CN = 0x84; //-- Enable ADC0, Continuous Tracking
// Mode, Conversion initiated on Timer
// 3 overflow, ADC0 data is right
// justified
EIE2 |= 0x02; //-- Enable ADC Interrupts
}
//--------------------------------------------------------------
void ADC0_ISR (void) interrupt 15
{
AD0INT = 0; //-- Clear ADC0 conversion complete
// interrupt flag
ADC0_reading = ADC0; //-- Read ADC0 data
}
Notes: <number>
<footer>
<header>
<date/time>
Sample code for detecting end-of-conversion using interrupt method. The ADC0 ISR will be executed automatically when the conversion is complete. The ADC0 register is read inside the ADC0 ISR. It is important to clear the AD0INT flag inside the ISR.

## Slide 34: Appendix

## Slide 35: 8-Bit ADC (ADC1)
Notes: <number>
<footer>
<header>
<date/time>
The operation of ADC1 is similar to ADC0. So, the ADC1 section need not be discussed in class, and can be left as an appendix.
This diagram shows the various blocks and SFRs of the 8-Bit ADC module which is referred to as ADC1. It has lower resolution compared to ADC0 but operates at a much higher speed. It operates at 500 ksps (kilo samples per second) conversion rate. Is has only single-ended inputs. There are no dedicated hardware pins for the ADC1 inputs; Port 1 pins are used for the ADC1 inputs. The ADC conversion can be started in five different ways. The converted digital value is available in the register ADC1.

## Slide 36: 8-Bit ADC (ADC1)
The ADC1 subsystem consists of:
  8-channel, configurable analog multiplexer (AMUX1)
  Programmable gain amplifier (PGA1)
    Default gain is 0.5
    Gain can be programmed to be 0.5, 1, 2 or 4
  8 bit SAR ADC
ADC1 is enabled by setting AD1EN (ADC1CN.7) to 1
Notes: <number>
<footer>
<header>
<date/time>
  The Programmable gain amplifier (PGA1) has a default gain of 0.5. The gain can be programmed to be 0.5, 1, 2 or 4 by programming the AMP1GN1-0 bits in the ADC1CF (ADC1 Configuration) Register. This register will be discussed later in another slide. The entire ADC0 is enabled/disabled by setting/resetting the AD1EN (ADC1CN.7) bit.

## Slide 37: Starting ADC1 Conversions
Conversions can be started in 5 different ways, depending on the ADC1 start of conversion mode bits (AD1CM2-0) in register ADC1CN
  Software command (writing 1 to AD1BUSY)
  Overflow of timer 2
  Overflow of timer 3
  External signal input (Rising edge of CNVSTR)
  Writing ‘1’ to the AD0BUSY (ADC0CN.4). (i.e., initiate conversion of ADC1 and ADC0 with a single software command)
During conversion, the AD1BUSY bit remains set to 1 and is restored to 0 when the conversion is complete
The falling edge of AD1BUSY triggers an interrupt (when enabled) and sets the AD1INT interrupt flag
Converted data is stored in the ADC1 data word register, ADC1
Notes: <number>
<footer>
<header>
<date/time>
ADC1 conversions can be started in five different ways - Software command (i.e. by writing 1 to AD1BUSY bit), Overflow of Timer 2, Overflow of Timer 3, External signal input (rising edge of CNVSTR) and by writing ‘1’ to the AD0BUSY (ADC0CN.4) bit. The last method enables initiation of conversion of ADC1 and ADC0 with a single software command. The conversion start method is selected by programming the AD1CM2-0 bits in ADC1CN register.
While the conversion is in progress, the AD1BUSY bit remains set to 1. It is restored to 0 when the conversion is complete. On the falling edge of AD1BUSY, the AD1INT interrupt flag (ADC1CN.5) is set. In a polling method, one can check the status of AD1INT flag to detect the completion of conversion.
If ADC1 End-of-Conversion Interrupt (EIE2.3) is enabled, then an interrupt will be generated and the corresponding ADC1 ISR will also be executed.

## Slide 38: Data Word Conversion Map (8-bit)
The mapping of the ADC1 analog inputs to the ADC1 data word register is much simpler
There is only one mode of input and the data word does not need to be justified
AIN1.0 – AGND (Volts) | ADC1
 | FFH
 | 80H
 | 7FH
0 | 00H
Notes: <number>
<footer>
<header>
<date/time>
For gain set to 1, the input voltage range is from 0 to (VREF*255/256).

## Slide 39: Programming ADC1
ADC1 can be programmed through the following sequence
  Step 1: configure the voltage reference (REF0CN)
  Step 2: configure appropriate pins on Port 1 as analog input (P1MDIN)
  Step 3: set the SAR1 conversion clock frequency and PGA1 gain (ADC1CF)
  Step 4: select the desired multiplexer input channel (AMX1SL).
  Step 5: set the appropriate control bits and start of conversion mode and turn on ADC1 (ADC1CN)
Notes: <number>
<footer>
<header>
<date/time>
The various SFRs used to control and manage the ADC1 are REF0CN, PIMDIN, ADC1CF, AMX1SL and ADC1CN. The programming sequence for ADC1 are enumerated in this slide.
For ADC1, the voltage reference could be from VREF1 or the AV+. This is achieved by programming the AD1VRS (REF0CN.3) bit. VREF1 may be connected to VREF (i.e. the internal voltage generator) or an external voltage reference.

## Slide 40: ADC1CF—ADC1 Configuration Register
Bit | Symbol | Description
7-3 | AD1SC4-0 | ADC1 SAR Conversion Clock frequency Bits SAR Conversion clock is derived from system clock by the following equation, where AD1SC refers to the 5-bit value in AD1SC4-0, and CLKSAR1 refers to the desired ADC1 SAR conversion clock frequency.
2 | - | UNUSED. Read=0, Write=don’t care
1-0 | AMP1GN1-0 | ADC1 Internal Amplifier Gain (PGA) 00: Gain = 0.5 01: Gain = 1 10: Gain = 2 11: Gain = 4
Notes: <number>
<footer>
<header>
<date/time>
This table shows the various bits of ADC1CF (ADC1 Configuration) Register that must be programmed to (a) set the gain of the PGA (b) set the SAR1 Conversion Clock Frequency.

## Slide 41: SAR1 Conversion Clock Frequency
The conversion clock has a maximum frequency of 6 MHz
The conversion clock frequency is calculated using the following equation:
Notes: <number>
<footer>
<header>
<date/time>
For ADC0, the SAR conversion clock has a maximum frequency of 6 MHz. The SAR conversion clock frequency depends on the System Clock Frequency and the value of the bits AD1SC4-0 in the ADC1CF (ADC1 Configuration) register.

## Slide 42: AMX1SL—AMUX1 Channel Select Register
Bit | Symbol | Description
7-3 | - | UNUSED. Read=00000, Write=don’t care
3-0 | AMX1AD2-0 | AMX1 Address Bits 000: AIN1.0 selected 001: AIN1.1 selected 010: AIN1.2 selected 011: AIN1.3 selected 100: AIN1.4 selected 101: AIN1.5 selected 110: AIN1.6 selected 111: AIN1.7 selected
Notes: <number>
<footer>
<header>
<date/time>
Selecting the channel for conversion is a matter of programming the AMX1AD2-0 bits in the AMX1SL (AMUX1 Channel Select) Register as per the table shown in this slide.

## Slide 43: ADC1CN—ADC1 Control Register
Notes: <number>
<footer>
<header>
<date/time>
The ADC1CN (ADC1 Control) Register is programmed to enable/disable ADC0, select the start of conversion mode and tracking mode. It also has the flag (AD1INT) to monitor the end-of-conversion. AD1BUSY flag can be set to start a conversion and it remains set till the conversion is complete.

## Slide 44: Detecting ADC1 End-of-Conversion
Polling Method
  AD1INT bit (ADC1CN.5) may be polled to determine when a conversion has completed
  Once the bit is set, read the ADC1 data
Interrupt Method
  If ADC1 end-of-conversion interrupt (EIE2.3) and global interrupts are enabled, then an interrupt will be generated and the appropriate ADC1 ISR will be executed
  Inside the ADC1 ISR, read the ADC1 data
Notes: <number>
<footer>
<header>
<date/time>
There are two ways to detect the end-of-conversion – Polling method by monitoring the AD1INT bit (ADC1CN.5), and Interrupt method by enabling the EIE2.3 bit.

## Slide 45: ADC1 Programming Example—Polling Method
void Init_ADC1(void)
{
REF0CN = 0x03; //-- Enable internal bias generator and
// internal reference buffer
// Select ADC1 reference from VREF1 pin
ADC1CF = 0x81; //-- SAR1 conversion clock=941KHz approx., Gain=1
AMX1SL = 0x00; //-- Select AIN1.0 input
ADC1CN = 0x82; //-- Enable ADC1, Continuous Tracking Mode,
// Conversion initiated on Timer 3 overflow
}
//--------------------------------------------------------------
// Interrupt Service Routine
void Timer3_ISR (void) interrupt 14
{
TMR3CN &= ~(0x80); //-- Clear TF3 flag
//-- Wait for ADC1 conversion to be over
while ( (ADC1CN |= 0x20) == 0); //-- Poll for AD1INT-->1
ADC1_reading = ADC1; //-- Read ADC1 data
ADC1CN &= 0xDF; //-- Clear AD1INT
}
Notes: <number>
<footer>
<header>
<date/time>
Sample code for detecting end-of-conversion using polling method. Timer 3 overflow starts the conversion. Inside the Timer 3 ISR, we poll the AD1INT bit and wait for it to be set to 1 before reading the ADC1 register.

## Slide 46: ADC1 Programming—Interrupt Method
Instead of using the polling technique as illustrated in the code on the previous slide, we could also use interrupt method
The ADC1 interrupt can be enabled by setting EADC1 (EIE2.3) and enabling global interrupts
The ISR for ADC1 will be called each time the conversion is completed
Inside the ISR, we simply need to:
  Read the ADC1 register
  Store the value in a variable
  Clear the AD1INT flag
Notes: <number>
<footer>
<header>
<date/time>

## Slide 47: www.silabs.com/MCU