## Slide 1: Lecture 1
Course Overview and
The 8051 Architecture
Notes: This lecture gives a quick introduction to the basic 8051 microcontroller. C8051F020 is backward compatible with 8051. Hence, any program written for the 8051 will work on C8051F020. Many of the features of C8051F020 are same as in the basic 8051, thus knowing the basic features of 8051 will help in understanding the C8051F020.

## Slide 2: MCUniversity Program Lectures
8051 architecture
System overview of C8051F020
8051 instruction set
System clock, crossbar and GPIO
Assembler directives
Programming using C language
Interrupts
Timer operations and programming
Serial communication
DAC and comparator
ADC
Notes: <number>
<footer>
<header>
<date/time>
Course goals.

## Slide 3: Course Syllabus
  Lectures and Tutorial questions are based on the “Embedded Programming with Field-Programmable Mixed-Signal Microcontrollers” Textbook

## Slide 4: Course Goals
At the end of this course, you should be able to:
  Understand the architecture of one of the most popular microcontroller (MCU) families
  Use an integrated development environment (IDE) to program and debug an MCU
  Program an MCU using Assembly and C languages
  Understand and use peripherals integrated into an MCU
  Interface an MCU to simple external components
  Understand and use interrupts
  Use timers in various modes
  Communicate using a serial interface
  Understand and use analog to digital converters (ADC), digital to analog converters (DAC) and comparators
Notes: <number>
<footer>
<header>
<date/time>
Course goals.

## Slide 5: Course Prerequisites
A course in Electric Circuits that includes understanding basic electronic components such as resistors, capacitors, diodes and transistors
A course in basic digital logic design that includes logic gates and Boolean arithmetic
Ability to program in a high-level programming language such as C or C++
Notes: <number>
<footer>
<header>
<date/time>
Prerequisites

## Slide 6: The 8051 Architecture
Microprocessors and microcontrollers
The 8051 microcontroller: a brief history
Block diagram of the original 8051
Is 8-bit still relevant?
Harvard and von Neumann architectures
Memory organization
Special function registers
Notes: <number>
<footer>
<header>
<date/time>
Contents of this lecture.

## Slide 7: Microprocessors and Microcontrollers
Microprocessor: general-purpose CPU
  Emphasis is on flexibility and performance
  Generic user-interface such as keyboard, mouse, etc.
  Used in a PC, PDA, cell phone, etc.
Microcontroller: microprocessor + memory on a single chip
  Emphasis is on size and cost reduction
  The user interface is tailored to the application, such as the buttons on a TV remote control
  Used in a digital watch, TV remote control, car and many common day-to-day appliances
Notes: <number>
<footer>
<header>
<date/time>
Differences between Microprocessors and Microcontrollers.

## Slide 8: Terminology
Integrated Circuit (IC): A miniaturized electronic circuit that consists of semiconductor devices and passive components contained in a package
Central Processing Unit (CPU): This refers to the core of the MCU that executes code
Microcontroller Unit (MCU): This is the standard acronym used for microcontrollers, and refers to the full IC that contains the CPU and peripherals.
“n-bit” – the “n” refers to the data bus width of the CPU, and is the maximum width of data it can handle at a time
  Examples: 8-bit MCU, 32-bit MCU
Notes: <number>
<footer>
<header>
<date/time>
Common terminology.

## Slide 9: Microcontroller Architectures
Microcontroller architecture refers to the internal hardware organization of a microcontroller
Each hardware architecture has its own set of software instructions called assembly language that allows programming of the microcontroller
Some of the popular microcontroller architectures
  Intel 8051
  Zilog Z80
  Atmel AVR
Notes: <number>
<footer>
<header>
<date/time>
What is architecture, and examples of microcontroller architectures.

## Slide 10: The 8051 Microcontroller—A Brief History
In 1980, Intel introduced the 8051, relevant today after more than two decades
First device in the MCS-51® family of 8-bit microcontrollers
In addition to Intel there are other second source suppliers of the ICs, who make microcontrollers that are compatible with the 8051 architecture.
In recent years some companies have incorporated many different and additional features into 8051
In 2000, Silicon Laboratories introduced a field programmable, mixed-signal chip (C8051F020) based on the 8051 core CPU
  This will be the platform for this course.
Notes: <number>
<footer>
<header>
<date/time>
8051 has been around for many many years. It is as popular today as it was in 1980. Manufacturers have enhanced the features of 8051. Silicon Labs is a leading manufacturer of 8051 based microcontroller.

## Slide 11: Is 8-bit Still Relevant?
“n-bit” – the “n” refers to the data bus width of the CPU, and is the maximum width of data it can handle at a time
PCs with 64-bit microprocessors are becoming common
Over 55% of all processors sold per year are 8-bit processors, which comes to over 3 billion of them per year!*
8-bit microcontrollers are sufficient and cost-effective for many embedded applications
More and more advanced features and peripherals are added to 8-bit processors by various vendors
8-bit MCUs are well-suited for low-power applications that use batteries
*Note: Statistics from Embedded.com Article ID# 9900861, Dec 2002
Notes: <number>
<footer>
<header>
<date/time>
Why are we learning 8-bit micros when 64-bit processors are now available? Are the 8-bit micros still used?

## Slide 12: Example System: RC Car
Notes: <number>
<footer>
<header>
<date/time>
Example system: RC Car – remote control section

## Slide 13: Block Diagram of the Original 8051
Notes: <number>
<footer>
<header>
<date/time>
Only 2 timers and 1 UART for serial communication. Four digital I/O ports. No analog features. 8051 memory can be extended by connecting external memory.

## Slide 14: Block Diagram of the Silicon Labs 8051
Notes: <number>
<footer>
<header>
<date/time>
C8051F020 block diagram showing all peripherals.

## Slide 15: Harvard and von Neumann Architectures
Harvard Architecture—a type of computer architecture where the instructions (program code) and data are stored in separate memory spaces
  Example: Intel 8051 architecture
von Neumann Architecture—another type of computer architecture where the instructions and data are stored in the same memory space
  Example: Intel x86 architecture (Intel Pentium, AMD Athlon, etc.)
Notes: <number>
<footer>
<header>
<date/time>
Basic difference between two of the most common types of architectures.

## Slide 16: MCU Fetch-Execute Cycle
Fetch operation—retrieves an instruction from the location in code memory pointed to by the program counter (PC)
Execute operation—executes the instruction that was fetched during the fetch operation. In addition to executing the instruction, the CPU also adds the appropriate number to the PC to point it to the next instruction to be fetched.
Notes: <number>
<footer>
<header>
<date/time>
PC points to code memory from where the next instruction will be fetched from. While the CPU executes the current instruction, it also increments PC (by one or more bytes) so that it points to the next instruction to be fetched.

## Slide 17: 8051 and 8052
The feature set of the 8052 is the superset of the 8051
In addition to all the features of the 8051, the 8052 includes
  128 bytes internal RAM (total of 256 bytes)
  A third 16-bit timer, with new modes of operation
  Additional SFRs to support the third timer
The Silicon Labs C8051F020 builds upon the 8052, and adds further features
The term “8051” is typically used in place of “8052”, and also refers to the 8051 architecture
Notes: <number>
<footer>
<header>
<date/time>
Differences between 8051 and 8052.

## Slide 18: C8051F020 Data Memory (RAM)
Internal Data Memory space is divided into three sections
  Lower 128
  Upper 128
  Special function register (SFR)
There are 384 bytes of memory space physically, though the Upper 128 and SFRs share the same addresses from location 80H to FFH.
Appropriate instructions should be used to access each memory block
Notes: <number>
<footer>
<header>
<date/time>
The Internal Data Memory space is divided into three sections- the Lower 128 bytes, the Upper 128 bytes and the SFR (Special Function Registers). This memory arrangement is the same in C8051F020.

## Slide 19: Lower 128—Register Banks and RAM
Bit-addressable Area (16 bytes)
Register Banks (8 bytes per bank; 4 banks)
General Purpose RAM (80 bytes)
Notes: <number>
<footer>
<header>
<date/time>
This diagram shows the layout of the lower 128 bytes of memory. The various sections are described on the next slide.

## Slide 20: Special Function Registers (SFRs)
SFRs provide control and data exchange with the microcontroller’s resources and peripherals
Registers which have their byte addresses ending with 0H or 8H are byte- as well as bit- addressable
Some registers are not bit-addressable. These include the stack pointer (SP) and data pointer register (DPTR)
Notes: <number>
<footer>
<header>
<date/time>
This diagram shows the various SFRs. C8051F020 has a lot many more SFRs compared to 8051 !!
Registers which have addresses ending with 0H or 8H are byte- as well as bit- addressable, such as P0, TCON, P1, SCON etc.

## Slide 21: Summary of SFRs
Accumulator (ACC) and B register
  ACC (also referred to as A) is used implicitly by several instructions
  B is used implicitly in multiply and divide operations
  These registers are the input/output of the arithmetic and logic unit (ALU)
Program status word—PSW
  Shows the status of arithmetic and logical operations using multiple bits such as Carry
  Selects the Register Bank (Bank 0 - Bank 3)
Stack pointer—SP
Data pointer—DPTR (DPH and DPL)
  16-bit register used to access external code or data memory
Timer Registers—TH0, TL0, TH1, TL1, TMOD, TCON
  Used for timing intervals or counting events
Parallel I/O Port Registers—P0, P1, P2 and P3
Serial Communication Registers—SBUF and SCON
Interrupt Management Registers—IP and IE
Power Control Register—PCON
Notes: <number>
<footer>
<header>
<date/time>
As you can see on this slide, there are registers to configure the UART, Timers etc.
Registers such as IP and IE are used to mange the interrupts – enable/disable them, set priorities etc.
Registers such as SBUF, P0 to P3 are used to exchange data with peripherals connected to the serial port of digital I/O ports.

## Slide 22: www.silabs.com/MCU