## Slide 1: Lecture 5
System Clock, Crossbar and GPIO

## Slide 2: System Clock, Crossbar and GPIO
Introduction to system clock
  Internal oscillator
  External oscillator
  Initializing system clock
Watchdog timer
Port pin
  Output modes
  Configuring port pins as digital inputs
Crossbar
  Crossbar pin assignment and allocation priority
  Enabling the crossbar
  XBR0 (Crossbar Register 0)
  XBR1 (Crossbar Register 1)
  XBR2 (Crossbar Register 2)
Notes: <number>
<footer>
<header>
<date/time>
In this lecture we will look at programming the system clock, the watchdog timer and the Digital Crossbar.
We will also discuss how to set the port pin output modes and how to set port pins for input operations.

## Slide 3: Introduction to the System Clock
The system clock can be considered the “heart-beat” of the microcontroller
The C8051F020 microcontroller may be operated from either an internal or an external clock source
Max system clock: 25 MHz
Internal oscillator: 16 MHz  20%
External oscillator options
  Crystal, capacitor, RC, CMOS clock
Notes: <number>
<footer>
<header>
<date/time>
The picture shows the different types of external clock generators - RC/C, Crystal or CMOS clock.

## Slide 4: Internal Oscillator
Upon reset, the MCU operates from the internal oscillator at a typical frequency of 2.0 MHz by default
It may be configured by software to operate at other typical frequencies of 4.0 MHz, 8.0 MHz or 16 MHz
The accuracy of the internal oscillator is  20%
Many applications that do not need a very accurate clock source will find the internal oscillator sufficient
Notes: <number>
<footer>
<header>
<date/time>
The C8051F020 micro-controller may be operated from an external oscillator or an internal oscillator. The internal oscillator may be configured to operate at 2Mhz, 4.0Mhz, 8.0MHz or 16MHz. An external 22.1184 MHz crystal is installed on the development board and is useful in providing a system clock frequency suitable for high baud rate generation for UART.

## Slide 5: Internal Oscillator Control Register (OSCICN)
Upon reset, the value in this register is set to 00010100b
This configures the internal oscillator to generate a frequency of 2 MHz
Bit | Symbol | Description
7 | MSCLKE | Missing Clock Enable Bit 0: Missing Clock Detector Disabled 1: Missing Clock Detector Enabled. The reset is triggered if clock is missing for more than 10ms
6-5 | Unused | Read = 00b, Write = don’t care
4 | IFRDY | Internal Oscillator Frequency Ready Flag 0: Internal Oscillator Frequency not running at speed specified by the IFCN bits. 1: Internal Oscillator Frequency is running at speed specified by the IFCN bits.
3 | CLKSL | System Clock Source Select Bit 0: Uses Internal Oscillator as System Clock 1: Uses External Oscillator as System Clock
2 | IOSCEN | Internal Oscillator Enable Bit 0: Internal Oscillator Disabled 1: Internal Oscillator Enabled
1-0 | IFCN1- IFCN 0 | Internal Oscillator Frequency Control Bit 00: Internal Oscillator typical frequency is 2 MHz 01: Internal Oscillator typical frequency is 4 MHz 10: Internal Oscillator typical frequency is 8 MHz 11: Internal Oscillator typical frequency is 16 MHz
Notes: <number>
<footer>
<header>
<date/time>
The internal oscillator frequency is chosen by programming the bits 0 and 1 (IFCN1-IFCN0) of OSCICN SFR.
Upon reset, the default value of the internal oscillator frequency is 2 MHz. After enabling internal oscillator (IOSCEN) and selecting Internal oscillator as system clock, one must wait for the IFRDY bit to be set high. When this bit is set high, it means that the Internal Oscillator Frequency is running at speed specified by the IFCN bits.

## Slide 6: External Oscillator
The external oscillator circuit supports four types of external clock sources
  Crystal
    Used if accurate clock is needed
  Capacitor
    Used for low-power operation at low frequencies
    Inexpensive
  Resistor-capacitor (RC)
    Same as capacitor
  CMOS Clock
    Used if an external CMOS clock is available
    Helpful if used as a common clock for multiple devices that need to communicate synchronously
Notes: <number>
<footer>
<header>
<date/time>
Various external oscillator options, and typical usage scenarios.

## Slide 7: External Crystal
An external crystal is installed on the ToolStick MCUniversity daughter card when shipped from the factory
  Crystals have a typical frequency accuracy of 0.1% or better
  The frequency of the crystal installed on the ToolStick DC is 22.1184 MHz
  This specific crystal frequency is chosen because it is especially useful in providing a system clock frequency suitable for high baud rate generation for serial port communication (UART)
Notes: <number>
<footer>
<header>
<date/time>
The C8051F020 micro-controller may be operated from an external oscillator or an internal oscillator. The internal oscillator may be configured to operate at 2Mhz, 4.0Mhz, 8.0MHz or 16MHz. An external 22.1184 MHz crystal is installed on the development board and is useful in providing a system clock frequency suitable for high baud rate generation for UART.

## Slide 8: External Oscillator Control Register (OSCXCN)
Bit | Symbol | Description
7 | XTLVLD | Crystal Oscillator Valid Flag 0: Crystal Oscillator is unused or not yet stable 1: Crystal Oscillator is running and stable
6-4 | XOSCMD2-0 | External Oscillator Mode Bits 00x: Off. XTAL1 pin is grounded internally. 010: System Clock from External CMOS Clock on XTAL1 pin. 011: System Clock from External CMOS Clock on XTAL1 pin divided by 2. 10x: RC/C Oscillator Mode with divide by 2 stage. 110: Crystal Oscillator Mode 111: Crystal Oscillator Mode with divide by 2 stage
3 | Reserved | Read = undefined, Write = don’t care
2-0 | XFCN2-0 | External Oscillator Frequency Control Bit
Upon reset, the value in this register is set to 00000000b
Bits 2-0: A table in the ‘F020 datasheet shows the appropriate values for the XFCN bits based on the desired external oscillator frequency
Bits 6-4: The XOSCMD bits configure the external oscillator type (Crystal, RC, etc.)
  See the ‘F020 datasheet for the values
Notes: <number>
<footer>
<header>
<date/time>
This table shows purpose of the various bits in the OSCXCN register. These are explained in the next slide.

## Slide 9: External Crystal Starting Procedure
Configure the External Oscillator
OSCXCN[6:0]
Wait for at least 1 ms
(Delay loop or timer)
Is
XTLVLD
== 1?
Switch from internal to
External oscillator
(CLKSL bit in OSCICN)
YES
NO
Notes: <number>
<footer>
<header>
<date/time>
If the crystal frequency is greater than 6.7 MHz, bits 2-0 (XFCN2-0) must be set to 111.
Bits 6-4 (XOSCMD2-0) are programmed based on the external oscillator whether it is RC/C, Crystal or CMOS clock on XTAL1. The external clock frequency may be divided by 2 if required.
After the external oscillator has been enabled by setting CLKSL (OSCICN.3) to 1, one must wait for the crystal oscillator to be stable. This can be checked by polling bit 7 (XTLVLD) of OSCXCN.

## Slide 10: Initializing System Clock
void Init_Ext_Clock(void)
{
unsigned int i;
OSCXCN = 0x67; //-- 0110 0111b
//-- External Osc Freq Control Bits (XFCN2-0) set
// to 111 because crystal frequency > 6.7 MHz
//-- Crystal Oscillator Mode (XOSCMD2-0) set to 110
//-- For Crsytal Oscillator Mode with divide-by-2 stage
// OSCXCN = 0x77;
for (i=9000; i>0; i--); // Wait at least 1 ms
//-- Wait till XTLVLD pin is set
while ( !(OSCXCN & 0x80) );
OSCICN = 0x88; //-- 1000 1000b
//-- Bit 2 : Internal Osc. disabled (IOSCEN = 0)
//-- Bit 3 : Uses External Oscillator as System
// Clock (CLKSL = 1)
//-- Bit 7 : Missing Clock Detector Enabled (MSCLKE = 1)
}
Notes: <number>
<footer>
<header>
<date/time>
This code segment shows you how to set up the external oscillator for the system clock. The missing clock detector has been enabled. When enabled, if the system clock goes missing for more than 100 micro-seconds, a reset will be generated. You have to wait at least 1 ms before polling on the XTLVLD bit to eliminate false positives.

## Slide 11: Watchdog Timer
The MCU has a programmable watchdog timer (WDT) which runs off the system clock
An overflow of the WDT forces the MCU into the reset state
Before the WDT overflows, the application program must restart it
WDT is useful in preventing the system from running out of control, especially in critical applications
If the system experiences a software or hardware malfunction which prevents the software from restarting the WDT, the WDT will overflow and cause a MCU reset
Notes: <number>
<footer>
<header>
<date/time>
WDT is useful in preventing the system from running out of control, especially in critical applications.

## Slide 12: Watchdog Timer
After a reset, the WDT is automatically enabled and starts running at the default maximum time interval, which is 524 ms for a 2 MHz system clock
The WDT consists of a 21-bit timer running from the programmed system clock
  A WDT reset is generated when the period between specific writes to its control register exceeds the programmed limit
The WDT may be enabled or disabled by software
  It may also be locked to prevent accidental disabling.
Once locked, the WDT cannot be disabled until the next system reset
It may also be permanently disabled. The watchdog features are controlled by programming the watchdog timer control register (WDTCN)
The last reset source can be checked by reading the reset sources (RSTSRC) register
Notes: <number>
<footer>
<header>
<date/time>
The WDT can be permanently disabled by software.

## Slide 13: Watchdog Timer Control Register (WDTCN)
Bit | Description
7-0 | WDT Control Writing 0xA5 both enables and reloads the WDT Writing 0xDE followed within 4 system clocks by 0xAD disables the WDT Writing 0xFF locks out the disable feature
4 | Watchdog Status Bit (when Read) Reading this bit indicates the Watchdog Timer Status 0: WDT is inactive 1: WDT is active
2-0 | Watchdog Timeout Interval Bits These bits set the Watchdog Timer Interval. When writing these bits, WDTCN.7 must be set to 0.
Notes: <number>
<footer>
<header>
<date/time>
The watchdog features are controlled by programming the Watchdog Timer Control Register (WDTCN).
Watchdog Timeout Interval Bits (2-0) are programmed to set the Watchdog Timer Interval. When writing these bits, WDTCN.7 must be set to 0.
The interval is given by the following equation:
43+WDTCN [2-0] x Tsysclk
Tsysclk is the system clock period. For a 2 MHz system clock, the interval range that can be programmed is 0.032 ms to 524 ms.

## Slide 14: Setting WDT Interval
Bits 2-0 of WDTCN register control the watchdog timeout interval. The interval is given by the following equation:
43+WDTCN [2-0] x Tsysclk
Tsysclk is the system clock period
For a 2 MHz system clock, the interval range that can be programmed is 0.032 ms to 524 ms
When the watchdog timeout interval bits are written to the WDTCN register, the WDTCN.7 bit must be held at logic 0
The programmed interval may be read back by reading the WDTCN register
After a reset, WDTCN[2-0] reads 111b
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Disabling the WDT
//------------------------------------------------------------
// Basic blank C program that does nothing
// other than disable the watch dog timer
//------------------------------------------------------------
// Includes
//------------------------------------------------------------
#include <C8051F020_defs.h> //-- SFR declarations
void main (void)
{
// Disable watchdog timer
WDTCN = 0xde;
WDTCN = 0xad;
while(1); //-- Stops program from terminating
}
//------------------------------------------------------------
Notes: <number>
<footer>
<header>
<date/time>
This code segment shows how to disable the Watchdog Timer.

## Slide 16: Port Pin Output Modes
The output mode of each port pin on Ports 0 through 3 can be configured as either Open-Drain or Push-Pull
The default state is Open-Drain
In the Open-Drain configuration:
  Writing logic 0 to the associated bit in the Port Data register will cause the Port pin to be driven to GND
  Writing logic 1 will cause the Port pin to assume a high-impedance state
In the Push-Pull configuration:
  Writing logic 0 to the associated bit in the Port Data register will cause the Port pin to be driven to GND
  Writing logic 1 will cause the Port pin to be driven to VDD
Notes: <number>
<footer>
<header>
<date/time>
The output mode of each port pin on Ports 0 through 3 can be configured as either Open-Drain or Push-Pull. The default state is Open-Drain.

## Slide 17: Port Pin Output Modes
The output modes of the Port pins are determined by the bits in the associated PnMDOUT registers
For example, a logic 1 in P1MDOUT.6 will configure the output mode of P1.6 to Push-Pull; a logic 0 in P1MDOUT.6 will configure the output mode of P1.6 to Open-Drain
Until the Crossbar is configured and enabled, the output drivers are not enabled
Example:
P1MDOUT |= 0x40; //-- Enable P1.6 as push-pull output
Notes: <number>
<footer>
<header>
<date/time>
The output modes of the Port pins are determined by the bits in the associated PnMDOUT registers.

## Slide 18: Configuring Port Pins as Digital Inputs
A Port pin is configured as a digital input by setting its output mode to “Open-Drain” and writing a logic 1 to the associated bit in the Port Data register
For example, P3.7 is configured as a digital input by setting P3MDOUT.7 to a logic 0 and P3.7 to a logic 1
Example:
//-- Configure P3.7 for input
P3MDOUT &= 0x7F; //-- Write a logic 0 to set Open-Drain // Output mode
P3 |= 0x80; //-- write a logic 1 to P3.7
Notes: <number>
<footer>
<header>
<date/time>
A Port pin is configured as a digital input by setting its output mode to “Open-Drain” and writing a logic 1 to the associated bit in the Port Data register.

## Slide 19: P1MDIN (Port1 Input Mode Register)
Bit | Symbol | Description
7-0 | P1MDIN.[7:0] | Port 1 Input Mode Bits. 0: Port Pin is configured in Analog Input mode. The digital input path is disabled (a read from the Port bit will always return ‘0’). The weak pull-up on the pin is disabled. 1: Port Pin is configured in Digital Input mode. A read from the Port bit will return the logic level at the Pin. The state of the weak pull-up is determined by the WEAKPUD bit
Reset Value: 0xFF (digital input mode)
Clearing a bit here to enable analog input mode also does the following:
  Disables output drivers on the corresponding port pin
  Instructs the crossbar to skip the pin for peripheral assignment
Notes: <number>
<footer>
<header>
<date/time>
Port 1 can be used for Digital input or Analog input for the 8-bit ADC1. By default, it is configured for Digital input.
When configured in Analog Input mode, the digital input path is disabled and a read from the Port bit will always return ‘0’.

## Slide 20: Disabling Weak Pull-Ups
Weak pull-ups are useful for bidirectional data communication where an external strong pull-up is used
This enables both sides to be able to drive the wire high or low
By default, each port pin has an internal weak pull-up device enabled which provides a resistive connection (about 100 kΩ) between the pin and VDD
The weak pull-up devices can be globally disabled by writing logic 1 to the Weak Pull-up Disable bit (WEAKPUD, XBR2.7)
The weak pull-up is automatically deactivated on any pin that is driving a logic 0
Notes: <number>
<footer>
<header>
<date/time>
The weak pull-up devices can be globally enabled or disabled by software.

## Slide 21: Crossbar
Notes: <number>
<footer>
<header>
<date/time>
Many of the C8051F020’s peripherals (such as UART, Timer control inputs etc) do not have dedicated pins through which they may be accessed. Instead they are available through the four lower I/O ports (P0, P1, P2 and P3). Each of the pins on P0, P1, P2 and P3 can be defined as a General Purpose Input/Output (GPIO) pin or can be controlled by a digital peripheral. This is achieved by programming the Digital Crossbar which is essentially a programmable switching netwrok.

## Slide 22: Crossbar
Problem: Many peripherals/functions are available inside the MCU
  There are limited number of pins available to connect the peripherals to the outside world
Solution: Pick and choose the peripherals that are necessary for an application, and assign only those to external pins
  This is the function of the crossbar
  Based on the application, the system designer makes the decision as to which peripherals are enabled, and which pins are used
The C8051F020 has a rich set of digital resources like UARTs, system management bus (SMBus), timer control inputs and interrupts
  These peripherals do not have dedicated pins through which they may be accessed
  They are available through the four lower I/O ports (P0, P1, P2 and P3)
  Each of the pins on P0, P1, P2 and P3 can be defined as a general purpose input/output (GPIO) pin or can be assigned to a digital peripheral
  :ower ports have dual functionalities
  This flexibility makes the MCU very versatile
Notes: <number>
<footer>
<header>
<date/time>
Based on the application, a system designer would have to decide what capabilities are required and then allocate the necessary digital functions to the port pins by programming the Digital Crossbar registers.
This flexibility makes the MCU very versatile

## Slide 23: Crossbar Pin Assignment and Allocation Priority
Notes: <number>
<footer>
<header>
<date/time>
The table shows the order of priority in which the peripherals are allocated port pins. UART0 has the highest priority and CNVSTR has the lowest priority.
The table also lists the Crossbar Register bits that must be enabled to allocate port pins to a peripheral. For example, to use UART0, XBR0.2 (UART0EN) bit must be set. This will allocate P0.0 for Tx0 and P0.1 for Rx0. If SPI and SMBus are not enabled but UART1 is, by setting XBR2.2 (UART1EN), then P0.2 and P0.3 will be allocated for Tx1 and Rx1 respectively.

## Slide 24: Crossbar Pin Assignment and Allocation Priority
The crossbar has a priority order in which peripherals are assigned to pins
  UART0 has the highest priority and CNVSTR has the lowest priority
There are three configuration registers, XBR0, XBR1 and XBR2, which are programmed to accomplish the pin allocations
If the corresponding enable bits of the peripheral are set to a logic 1 in the crossbar registers, then the port pins are assigned to that peripheral
Pin assignments to associated functions are done in groups
  For example, TX0 and RX0 for UART0 are assigned together
Example: If the UART0EN bit (XBR0.2) is set to logic 1, the TX0 and RX0 pins will be mapped to the port pins P0.0 and P0.1, respectively.
  Since UART0 has the highest priority, its pins will always be mapped to P0.0 and P0.1 when UART0EN is set to logic 1 and will have precedence over any other peripheral allocation
Notes: <number>
<footer>
<header>
<date/time>
There are three configuration registers, XBR0, XBR1 and XBR2, which are programmed to accomplish the pin allocations.
Pin assignments to associated functions are done in groups, for example, Tx0 and Rx0 are assigned together.

## Slide 25: Enabling the Crossbar
The crossbar should be enabled once all the crossbar registers (XBR0, XBR1 and XBR2) have been configured
This is done by setting XBARE (XBR2.6) to a logic 1
All output drivers are disabled until the crossbar is enabled
//-- Configures the Crossbar and GPIO ports -------------------
void Init_Port(void)
{
P0MDOUT |= 0x01; //-- Enable TX0 as a push-pull output
P1MDOUT |= 0x40; //-- Enable P1.6 as push-pull output
XBR0 = 0x04; //-- Enable UART0
XBR1 = 0x00;
XBR2 = 0x40; //-- Enable Crossbar & weak pull-ups // (globally)
}
Notes: <number>
<footer>
<header>
<date/time>
XBARE (XBR2.6) must be set to a logic 1 in order to enable the Crossbar.

## Slide 26: XBR0 (Crossbar Register 0)
XBR0 SFR, upon reset, has a value 0x00
Bit | Symbol | Description
7 | CP0E | Comparator 0 Output Enable Bit. 0: CP0 unavailable at Port pin. 1: CP0 routed to Port pin.
6 | ECI0E | PCA0 External Counter Input Enable Bit. 0: PCA0 External Counter Input unavailable at Port pin. 1: PCA0 External Counter Input (ECI0) routed to Port pin.
5-3 | PCA0ME | PCA0 Module I/O Enable Bits. 000: All PCA0 I/O unavailable at Port pins. 001: CEX0 routed to Port pin. 010: CEX0, CEX1 routed to 2 Port pins. 011: CEX0, CEX1, and CEX2 routed to 3 Port pins. 100: CEX0, CEX1, CEX2, and CEX3 routed to 4 Port pins. 101: CEX0, CEX1, CEX2, CEX3, and CEX4 routed to 5 Port pins. 110: RESERVED 111: RESERVED
2 | UART0EN | UART0 I/O Enable Bit. 0: UART0 I/O unavailable at Port pins. 1: UART0 TX routed to P0.0, and RX routed to P0.1
1 | SPI0EN | SPI0 Bus I/O Enable Bit. 0: SPI0 I/O unavailable at Port pins. 1: SPI0 SCK, MISO, MOSI, and NSS routed to 4 Port pins.
0 | SMB0EN | SMBus0 Bus I/O Enable Bit. 0: SMBus0 I/O unavailable at Port pins. 1: SMBus0 SDA and SCL routed to 2 Port pins.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: XBR1 (Crossbar Register 1)
XBR1 SFR, upon reset, has a value 0x00
Bit | Symbol | Description
7 | SYSCKE | /SYSCLK Output Enable Bit. 0: /SYSCLK unavailable at Port pin. 1: /SYSCLK routed to Port pin.
6 | T2EXE | T2EX Input Enable Bit. 0: T2EX unavailable at Port pin. 1: T2EX routed to Port pin.
5 | T2E | T2 Input Enable Bit. 0: T2 unavailable at Port pin. 1: T2 routed to Port pin.
4 | INT1E | /INT1 Input Enable Bit. 0: /INT1 unavailable at Port pin. 1: /INT1 routed to Port pin.
3 | T1E | T1 Input Enable Bit. 0: T1 unavailable at Port pin. 1: T1 routed to Port pin.
2 | INT0E | /INT0 Input Enable Bit. 0: /INT0 unavailable at Port pin. 1: /INT1 routed to Port pin.
1 | T0E | T0 Input Enable Bit. 0: T0 unavailable at Port pin. 1: T0 routed to Port pin.
0 | CP1E | CP1 Output Enable Bit. 0: CP1 unavailable at Port pin. 1: CP1 routed to Port pin.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: XBR2 (Crossbar Register 2)
XBR2 SFR, upon reset, has a value 0x00
Bit | Symbol | Description
7 | WEAKPUD | Weak Pull-Up Disable Bit. 0: Weak pull-ups globally enabled. 1: Weak pull-ups globally disabled.
6 | XBARE | Crossbar Enable Bit. 0: Crossbar disabled. All pins on Ports 0, 1, 2, and 3, are forced to Input mode. 1: Crossbar enabled.
5 | - | UNUSED. Read = 0, Write = don't care.
4 | T4EXE | T4EX Input Enable Bit. 0: T4EX unavailable at Port pin. 1: T4EX routed to Port pin.
3 | T4E | T4 Input Enable Bit. 0: T4 unavailable at Port pin. 1: T4 routed to Port pin.
2 | UART1E | UART1 I/O Enable Bit. 0: UART1 I/O unavailable at Port pins. 1: UART1 TX and RX routed to 2 Port pins.
1 | EMIFLE | External Memory Interface Low-Port Enable Bit. 0: P0.7, P0.6, and P0.5 functions are determined by the Crossbar or the Port latches. 1: If EMI0CF.4 = ‘0’ (External Memory Interface is in Multiplexed mode) P0.7 (/WR), P0.6 (/RD), and P0.5 (ALE) are ‘skipped’ by the Crossbar and their output states are determined by the Port latches and the External Memory Interface. 1: If EMI0CF.4 = ‘1’ (External Memory Interface is in Non-multiplexed mode) P0.7 (/WR) and P0.6 (/RD) are ‘skipped’ by the Crossbar and their output states are determined by the Port latches and the External Memory Interface.
0 | CNVSTE | External Convert Start Input Enable Bit. 0: CNVSTR unavailable at Port pin. 1: CNVSTR routed to Port pin.
Notes: <number>
<footer>
<header>
<date/time>
For the digital crossbar to be enabled, XBARE (XBR2.6) must be set to 1.

## Slide 29: Ports 4 Through 7
All Port pins on Ports 4 through 7 can be accessed as general-purpose I/O (GPIO) pins by reading and writing the associated Port Data registers, a set of SFRs which are byte-addressable
A read of a port data register (or port bit) will always return the logic state present at the pin
The SFRs associated with ports 7 to 4 are P74OUT and the individual Port Data registers: P4, P5, P6 and P7
Bit | Symbol | Description
7 | P7H | Port7 Output Mode High Nibble Bit. 0: P7.[7:4] configured as Open-Drain. 1: P7.[7:4] configured as Push-Pull.
6 | P7L | Port7 Output Mode Low Nibble Bit. 0: P7.[3:0] configured as Open-Drain. 1: P7.[3:0] configured as Push-Pull.
5 | P6H | Port6 Output Mode High Nibble Bit. 0: P6.[7:4] configured as Open-Drain. 1: P6.[7:4] configured as Push-Pull.
4 | P6L | Port6 Output Mode Low Nibble Bit. 0: P6.[3:0] configured as Open-Drain. 1: P6.[3:0] configured as Push-Pull.
3 | P5H | Port5 Output Mode High Nibble Bit. 0: P5.[7:4] configured as Open-Drain. 1: P5.[7:4] configured as Push-Pull.
2 | P5L | Port5 Output Mode Low Nibble Bit. 0: P5.[3:0] configured as Open-Drain. 1: P5.[3:0] configured as Push-Pull.
1 | P4H | Port4 Output Mode High Nibble Bit. 0: P4.[7:4] configured as Open-Drain. 1: P4.[7:4] configured as Push-Pull.
0 | P4L | Port4 Output Mode Low Nibble Bit. 0: P4.[3:0] configured as Open-Drain. 1: P4.[3:0] configured as Push-Pull.
Notes: <number>
<footer>
<header>
<date/time>
Port Data Registers P4 to P7 are byte-addressable.
Unlike Ports 0 to 3 (where the output mode can be defined separately for every individual bit), the output mode for Ports 4 to 7 are defined in groups of 4 bits – the high and low nibbles. For example, if P7H (P74OUT.7) is set to 1, then the bits P7[7:4] are configured in Push-Pull output mode.

## Slide 30: www.silabs.com/MCU