## Slide 1: Lecture 9
Timer Operations and Programming

## Slide 2: Timer Operations and Programming
Introduction
Summary of timers
Timer programming sequence
Summary of timer SFRs
Timer 0: 8-bit auto-reload mode (mode 2)
  Programming sequence (timer 0 in mode 2)
  Generating Interrupts on timer 0 overflow
Timer 3: 16-bit auto-reload mode (mode 0)
  Timer 3 programming sequence
  Generating interrupts on timer 3 overflow
Timer 2: 16-bit auto-reload mode (mode 1)
  Timer 2: programming example
Timer 2: 16-bit counter/timer with capture (mode 0)
Notes: <number>
<footer>
<header>
<date/time>
In this lecture we will look at the timer operations and how to program them in different modes.

## Slide 3: Introduction
Timers are used for: interval timing, event counting or baud rate generation
In interval timing applications, a timer is programmed to overflow at a regular interval and the following:
    Set the timer overflow flag or
    Generate an interrupt
  The flag or interrupt is used to synchronise the program to perform an action such as checking the state of inputs and updating the DAC output or ADC input
  This can also be used to generate waveforms at set frequencies
Event counting is used to determine the number of occurrences of an event, rather than to measure the elapsed time between events. In this case, the timer functions as a counter.
  An “event” is any external stimulus that provides a high-to-low transition at the selected input pin
The timers can also function as the baud rate generators for the C8051F020’s internal serial ports (UART0 and UART1)
  “Baud rate” is the bit rate of the serial port (the time period of a bit)
Notes: <number>
<footer>
<header>
<date/time>
In interval timing applications, a timer is programmed to overflow at a regular interval and the event is used to synchronise the program to perform an action such as checking the state of inputs, changing the output of an I/O pin, initiating an ADC conversion etc. This can also be used to generate waveforms at set frequencies.
Event counting is used to determine the number of occurrences of an event, such as the presence of a pulse. In this case, the timer functions as a counter.
When we discuss Serial Communication, we will see how the timers may be programmed to generate a baud rate for UART.

## Slide 4: Summary of Timers
The C8051F020 has 5 counter/timers
Mode | Timer 0 & 1 | Timer 2 | Timer 3 | Timer 4
0 | 13-bit counter/timer | 16-bit counter/timer with capture | 16-bit timer with auto-reload | 16-bit counter/timer with capture
1 | 16-bit counter/timer | 16-bit counter/timer with auto-reload |  | 16-bit counter/timer with auto-reload
2 | 8-bit counter/timer with auto-reload (Baud rate Generator for UART0 and UART1, Timer 1 only) | Baud rate generator for UART0 |  | Baud rate generator for UART1
3 | Two 8-bit counter/timers (Timer 0 only) |  |  | 
Notes: <number>
<footer>
<header>
<date/time>
There are 5 Timers in C8051F020. These can be configured to operate in different modes. The various modes of operations for the timers are shown in this table. Timer 0 and Timer 1 are very similar in their operations. Same is true for Timer 2 and Timer 4. Timer 3 is the simplest of all, it has only one mode of operation. Timer 1, Timer 2 and Timer 4 are used to generate baud rate for serial communication.

## Slide 5: Timer Programming Sequence
For Timers 0 and 1
  Step 1: Select the desired clock by programming CKCON.3 (T0M) or CKCON.4 (T1M). The clock input may be the system clock or the system clock divided by 12.
  Step 2: Select the operating mode (T0M[1:0] or T1M[1:0] in TMOD)
  Step 3: Write the starting value for count up sequence into the associated count registers (TL0, TL1, TH0 and TH1)
  Step 4: [OPTIONAL] Enable timer interrupt (ET0 or ET1 in IE) and global interrupts (EA in IE)
  Step 5: Set the appropriate control bits, and turn on Timer (TR0 or TR1 in TCON)
Notes: <number>
<footer>
<header>
<date/time>
The programming sequence for timer 0 and 1 is as follows – select the desired clock, set the mode of operation, load the starting value in the timer count register and turn on the timer. In auto-reload mode, the reload register also needs to be loaded with a value.

## Slide 6: Timer Programming Sequence
For Timer 3
  Step 1: Write the auto-reload value into the auto-reload registers (TMR3RLL and TMR3RLH)
  Step 2: Write the starting value for count up sequence into the count registers (TMR3L and TMR3H)
  Step 3: Select the desired clock source (T3XCLK) and frequency (T3M) and set the control bits (TR3)
  Step 4: [OPTIONAL] Enable timer interrupt (ET3 in EIE2) and global interrupts (EA in IE)
  Step 5: Turn on Timer 3 (TMR3CN)
Note: “Auto-reload” means the hardware automatically reloads the count registers with the value from the reload register when the count overflows from 0xFFFF to 0x0000
Notes: <number>
<footer>
<header>
<date/time>
As mentioned earlier, Timer 3 is the simplest of all. It has only one mode of operation – the auto-reload mode. The programming sequence is as follows – load the auto-reload value into the auto-reload registers, write the starting value for count up sequence, select the desired clock frequency and start the timer.

## Slide 7: Timer Programming Sequence
For Timers 2 and 4
  Step 1: Select the desired system clock frequency (CKCON)
  Step 2: Write the auto-reload value into the associated capture registers if using auto-reload mode (RCAP2L, RCAP2H, RCAP4L and RCAP4H)
  Step 3: Write the starting value for count up sequence into the associated count registers (TL2, TL4, TH2 and TH4)
  Step 4: Select the mode (C/Tx, CP/RLx) and set the appropriate control bits (TRx)
  Step 5: [OPTIONAL] Enable timer interrupt (ET2 in IE or ET4 in EIE2) and global interrupts (EA in IE)
  Step 6: Turn on Timer (T2CON and T4CON)
Notes: <number>
<footer>
<header>
<date/time>
The programming sequence for timer 2 and 4 is as follows – select the desired clock frequency, load the auto-reload value, load the starting value for count up sequence, set the mode of operation and turn on the timer.

## Slide 8: Summary of Timer SFRs
Timer SFR | Affected Timers | Purpose | Address | Bit Addressable
CKCON | 0, 1, 2 and 4 | Clock Control | 8EH | No
TCON | 0 and 1 | Timer Control | 88H | Yes
TMOD |  | Timer Mode | 89H | No
TL0 |  | Timer 0 Low Byte | 8AH | No
TL1 |  | Timer 1 Low Byte | 8BH | No
TH0 |  | Timer 0 High Byte | 8CH | No
TH1 |  | Timer 1 High Byte | 8DH | No
T2CON | 2 | Timer 2 Control | C8H | Yes
RCAP2L |  | Timer 2 Low Byte Capture | CAH | No
RCAP2H |  | Timer 2 High Byte Capture | CBH | No
TL2 |  | Timer 2 Low Byte | CCH | No
TH2 |  | Timer 2 High Byte | CDH | No
Notes: <number>
<footer>
<header>
<date/time>
There are 22 SFRs used to access and control the timers. This table is a ready reference for the registers that need to be programmed for the various timers. Note that, except for TCON and T2CON registers, none of the other timer SFRs are bit-addressable.

## Slide 9: Summary of Timer SFRs
Timer SFR | Affected Timers | Purpose | Address | Bit Addressable
TMR3CN | 3 | Timer 3 Control | 91H | No
TMR3RLL |  | Timer 3 Low Byte Reload | 92H | No
TMR3RLH |  | Timer 3 High Byte Reload | 93H | No
TMR3L |  | Timer 3 Low Byte | 94H | No
TMR3H |  | Timer 3 High Byte | 95H | No
T4CON | 4 | Timer 4 Control | C9H | No
RCAP4L |  | Timer 4 Low Byte Capture | E4H | No
RCAP4H |  | Timer 4 High Byte Capture | E5H | No
TL4 |  | Timer 4 Low Byte | F4H | No
TH4 |  | Timer 4 High Byte | F5H | No
Notes: <number>
<footer>
<header>
<date/time>
Summary of Timer SFRs (continued from the previous slide)

## Slide 10: Timer 0: 8-Bit Auto-Reload Mode (Mode 2)
This mode configures Timers 0 (and 1) to operate as 8-bit counter/timers with automatic reload of the start value
The timer low byte (TLx) operates as an 8-bit timer while the timer high byte (THx) holds a reload value
When the count in TLx overflows from FFH to 00H, the timer flag is set and the value in THx is automatically loaded into TLx
Counting continues from the reload value up to the next FFH overflow, and so on
This mode is convenient for creating regular periodic intervals, as the timer overflows at the same rate once TMOD and THx are initialized
TLx must be initialized to the desired value before enabling the timer for the first count to be correct
Timer 1 can be used as an 8-bit baud rate generator for UART0 and/or UART1 in mode 2
Timer Counter Registers
Notes: <number>
<footer>
<header>
<date/time>
This functional block diagram shows the operation of Timer 0 in Mode 2 (8-bit auto-reload mode). TL0 is used as the 8-bit timer count register while TH0 is used as the 8-bit reload register. T0M bit in register CKCON decides whether SYSCLK or SYSCLK/12 is used. When the timer is enabled (by setting TR0 to logic “1”), TCLK starts triggering the count register. When the count register overflows (going from FFh to 00h), the timer overflow flag (TF0) will be set and the value in the reload register will be transferred to the count register. If the Timer 0 Overflow Interrupt has been enabled, then it will be generated and the corresponding ISR will be automatically executed.
Timer 0 may be triggered by an external source (T0) instead of SYSCLK. The crossbar will need to be programmed accordingly to make a pin available for T0 input.
In general, the rate at which the timer overflows can be controlled by changing the system clock frequency, choosing SYSCLK or SYSCLK/12, and choosing a different value for reload (in TH0).

## Slide 11: Timer 0: Programming Step 1
Select the desired clock by programming CKCON (Clock Control) Register
For Timer 0, program the bit T0M
Bit | Symbol | Description
7 | - | Unused. Read=000b; Write=Don’t care.
6 | T4M | Timer 4 Clock Select 0: Timer 4 uses the system clock divided by 12. 1: Timer 4 uses the system clock.
5 | T2M | Timer 2 Clock Select 0: Timer 2 uses the system clock divided by 12. 1: Timer 2 uses the system clock.
4 | T1M | Timer 1 Clock Select 0: Timer 1 uses the system clock divided by 12. 1: Timer 1 uses the system clock.
3 | T0M | Timer 0 Clock Select 0: Timer 0 uses the system clock divided by 12. 1: Timer 0 uses the system clock
2-0 | Reserved | Read=000b. Must Write=000b
Notes: <number>
<footer>
<header>
<date/time>
The next few slides elaborate on the steps required to program Timer 0 in Mode 2 (auto reload) operation. The details of the SFRs that need to be programmed are discussed.
This slide shows how to select the desired clock – SYSCLK or SYSCLK/12.

## Slide 12: Timer 0—Programming Step 1
It is very important that while configuring a timer you take care not to disturb the mode of other timers
What would happen if you did this?
CKCON |= 0x04; //-- T0M = 1; Timer 0 uses SysClock
CKCON &= 0xF0; //-- T0M = 0; Timer 0 uses SysClock/12
CKCON = 0x04;
Notes: <number>
<footer>
<header>
<date/time>
Code segment to select the clock source for Timer 0.

## Slide 13: Timer 0—Programming Step 2
Select the operating mode by programming the TMOD (Timer Mode) register
Bit | Symbol | Description
7 | GATE1 | Timer 1 Gate Control 0: Timer 1 enabled when TR1(TCON.6)=1 irrespective of /INT logic level 1: Timer 1 enabled only when TR1=1 AND /INT=logic 1
6 | C/T1 | Counter/Timer 1 Select 0: Timer Function: Timer 1 incremented by clock defined by T1M bit (CKCON.4). 1: Counter Function: Timer 1 incremented by high- to-low transition on external input pin (T1).
5-4 | T1M1- T1M0 | Timer 1 Mode Select
3 | GATE0 | Timer 0 Gate Control 0: Timer 0 enabled when TR0(TCON.4)=1 irrespective of /INT logic level 1: Timer 0 enabled only when TR0=1 AND /INT=logic 1
2 | C/T0 | Counter/Timer 0 Select 0: Timer Function: Timer 0 incremented by clock defined by T0M bit (CKCON.3). 1: Counter Function; Timer 0 incremented by high- to-low transition on external input pin (T0).
1-0 | T0M1-T0M0 | Timer 0 Mode Select
//-- Timer 0 in Mode 2
//-- Set T0M[1:0] to 10b
TMOD &= ~0x03;
TMOD |= 0x02;
Notes: <number>
<footer>
<header>
<date/time>
Select the operating mode for Timer 0 by programming the T0M1 and T0M0 bits of the TMOD register.

## Slide 14: Timer 0/Timer 1 Mode Select Bits
TxM1 | TxM0 | Mode | Description
0 | 0 | 0 | 13 bit Counter/Timer
0 | 1 | 1 | 16 bit Counter/Timer
1 | 0 | 2 | 8 bit Counter/Timer with Auto-reload
1 | 1 | 3 | Timer 1: Inactive Timer 0: Two 8 bit Counter/Timers
x = 0 or 1 for Timer0 or Timer1
Notes: <number>
<footer>
<header>
<date/time>
This table shows the values to be loaded in TxM1 and TxM0 bits of the TMOD register to set up the mode of operation. (x is 0 or 1)
Only Timer 0 can be used in mode 3; Timer 1 does not have Mode 3 operation.

## Slide 15: Timer 0—Programming Step 3
Write the starting value for count up sequence in the appropriate register, TL0 in this case:
TL0 = 0xFF; //-- start value
Write the reload value in the appropriate register, TH0 in this case:
TH0 = 0x80; //-- reload value
Notes: <number>
<footer>
<header>
<date/time>
Write the starting value for count up sequence in the TL0 register. For the reload value to be loaded immediately after the timer is started, the count register (TL0) is loaded with FFh so that the first TCLK pulse will make the timer overflow.
The reload value is loaded in TH0. In this example, the timer will always count from 80h to FFh. When if overflows, the reload value loaded in the count register is 80h.

## Slide 16: Timer 0—Programming Step 5
Turn on the timer by programming the TCON (Timer Control) Register
Bit | Symbol | Description
7 | TF1 | Timer 1 Overflow Flag Set by hardware when Timer 1 overflows. This flag can be cleared by software but is automatically cleared when the CPU vectors to the Timer 1 interrupt service routine (ISR). 0: No Timer 1 overflow detected 1: Timer 1 has overflowed
6 | TR1 | Timer 1 Run Control 0: Timer 1 disabled 1: Timer 1 enabled
5 | TF0 | Timer 0 Overflow Flag Same as TF1 but applies to Timer 0 instead. 0: No Timer 0 overflow detected 1: Timer 0 has overflowed
4 | TR0 | Timer 0 Run Control 0: Timer 0 disabled 1: Timer 0 enabled
3 | IE1 | External Interrupt 1 This flag is set by hardware when an edge/level of type defined by IT1 is detected. It can be cleared by software but is automatically cleared when the CPU vectors to the External Interrupt 1 ISR if IT1=1. This flag is the inverse of the /INT1 input signal’s logic level when IT1=0
2 | IT1 | Interrupt 1 Type Select 0: /INT1 is level triggered 1: /INT1 is edge triggered
1 | IE0 | External Interrupt 0 Same as IE1 but applies to IT0 instead.
0 | IT0 | Interrupt 0 Type Select 0: /INT0 is level triggered 1: /INT0 is edge triggered
//--start Timer 0
//--(TCON.4 = 1)
TR0 = 1;
Notes: <number>
<footer>
<header>
<date/time>
Turn on the timer by setting TR0 (TCON.4) to 1.

## Slide 17: Generating Interrupts on Timer 0 Overflow
When the count in TLx overflows from FFH to 00H, the timer overflow flag is set in the TCON register
For Timer 0 it is TF0 in TCON register (TCON.5)
To detect when a timer overflows, there are two options:
  By polling the timer overflow bit
  By enabling the timer overflow interrupt
    This is done by programming the IE (interrupt enable) register
Notes: <number>
<footer>
<header>
<date/time>
When the count in TL0 overflows from FFH to 00H, the timer overflow flag (TF0) is set in the TCON register (TCON.5).
One can poll this bit to detect when the timer overflows or program the microcontroller to generate an interrupt each time the timer overflows.
This is done by programming the ET0 flag in the IE (Interrupt Enable) register.

## Slide 18: Interrupt Enable (IE) SFR
Bit | Symbol | Description
7 | EA | Enable All Interrupts 0: Disable all interrupt sources. 1: Enable each interrupt according to its individual mask setting.
6 | IEGF0 | General Purpose Flag 0 This is a general purpose flag for use under software control.
5 | ET2 | Enable Timer 2 Interrupt 0: Disable Timer 2 Interrupt. 1: Enable interrupt requests generated by TF2 (T2CON.7).
4 | ES0 | Enable UART0 Interrupt 0: Disable UART0 Interrupt. 1: Enable UART0 Interrupt.
3 | ET1 | Enable Timer 1 Interrupt 0: Disable Timer 1 Interrupt. 1: Enable interrupt requests generated by TF1 (TCON.7).
2 | EX1 | Enable External Interrupt 1 0: Disable external interrupt 1. 1: Enable interrupt request generated by the /INT1 pin.
1 | ET0 | Enable Timer 0 Interrupt 0: Disable Timer 0 Interrupt. 1: Enable interrupt requests generated by TF0 (TCON.5).
0 | EX0 | Enable External Interrupt 0 0: Disable external interrupt 0. 1: Enable interrupt request generated by the /INT0 pin.
ET0 = 1; // Enable interrupt
// request generated
// by Timer 0 overflow
// flag, TF0 (TCON.5)
Once the interrupt generation is enabled, the ISR is automatically executed when the timer overflows
Notes: <number>
<footer>
<header>
<date/time>
Program the ET0 flag (IE.1) to enable or disable the Timer 0 interrupt on overflow.

## Slide 19: Timer3: 16-Bit Auto-Reload Mode (Mode 0)
Timer 3 is always configured as an auto-reload timer, with the reload value held in TMR3RLL and TMR3RLH
TMR3CN is the only SFR required to configure Timer 3
Notes: <number>
<footer>
<header>
<date/time>
Timer 3 is always configured as an auto-reload timer, with the reload value held in TMR3RLL and TMR3RLH registers.
TMR3CN is the only SFR required to configure and control Timer 3. Timer 3 may be triggered using an external oscillator source (which is divided by 8), SYSCLK or SYSCLK/12. TR3 flag in TMR3CN register enables or disables the timer. Timer 3 overflows may also be used to initiate ADC conversion.

## Slide 20: Timer3: 16-Bit Auto-Reload Mode (Mode 0)
Timer 3 may be clocked by the external oscillator source (divided by 8) or the system clock (divided by 1 or 12 according to T3M)
When T3XCLK is set to 1, timer 3 is clocked by the external oscillator input (divided by 8) regardless of the system clock selection
When T3XCLK is 0, the timer 3 clock source is specified by bit T3M
Timer 3 can also be used to start an ADC Data Conversion
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Timer 3 Programming Sequence—Step 1a
Select the desired clock source (external oscillator or SYSCLK) by programming T3XCLK (TMR3CN.0)
Bit | Symbol | Description
7 | TF3 | Timer 3 Overflow Flag Set by hardware when Timer 3 overflows from FFFFH to 0000H. When the Timer 3 interrupt is enabled, setting this bit causes the CPU vectors to the Timer 3 ISR. This bit is not automatically cleared by hardware and must be cleared by software.
6-3 | UNUSED | Read=0000b, Write=don’t care
2 | TR3 | Timer 3 Run Control 0: Timer 3 disabled 1: Timer 3 enabled
1 | T3M | Timer 3 Clock Select 0: Counter/Timer 3 uses the system clock divided by 12. 1: Counter/Timer 3 uses the system clock.
0 | T3XCLK | Timer 3 External Clock Select 0: Timer 3 clock source defined by bit T3M (TMR3CN.1) 1: Timer 3 clock source is the external oscillator input divided by 8. T3M is ignored.
//-- Stop Timer 3,
//-- Clear TF3
//-- use SYSCLK/12
//-- timebase
TMR3CN = 0x00;
//-- use External
//-- Oscillator
TMR3CN |= 0x01;
Notes: <number>
<footer>
<header>
<date/time>
Select the desired clock source (External Oscillator or SYSCLK) by programming T3XCLK (TMR3CN.0) bit.

## Slide 22: Timer 3 Programming Sequence—Step 1b-2
If using SYSCLK, select whether divide-by-12 is required. Program the T3M (TMR3CN.1) bit.
TMR3CN |= 0x02; //-- use SYSCLK (NOT SYSCLK/12) timebase
Write the auto-reload value into the auto-reload registers (TMR3RLL+TMR3RLH or TMR3RL)
TMR3RL = 0xfff6;
Notes: <number>
<footer>
<header>
<date/time>
If using SYSCLK, select whether divide-by-12 is required or not by programming the T3M (TMR3CN.1) bit.
The reload value is held in the TMR3RLL and TMR3RLH registers. The 16-bit register may be accessed using the TMR3RL name. In this example, the timer will count from FFF6h to FFFFh and then overflow.

## Slide 23: Timer 3 Programming Sequence—Step 3 & 4
Write the starting value for count up sequence into the count registers (TMR3L+TMR3H or TMR3)
TMR3 = 0xffff; //-- set to reload immediately
Start the timer by setting TR3 (TMR3CN.2) to 1
TMR3CN |= 0x04; //-- Start Timer 3
Notes: <number>
<footer>
<header>
<date/time>
Write the starting value for count up sequence into the count registers (TMR3L+TMR3H or TMR3).
TR3 bit (TMR3CN.2) is used to enable or disable the timer.

## Slide 24: Extended Interrupt Enable 2 (EIE2) SFR
Bit | Symbol | Description
7 | EXVLD | Enable External Clock Source Valid (XTLVLD) Interrupt 0: Diable XTLVLD interrupt. 1: Enable interrupt requests generated by XTLVLD (OXCXCN.7)
6 | ES1 | Enable UART1 Interrupt 0: Disable UART1 Interrupt. 1: Enable UART1 Interrupt.
5 | EX7 | Enable External Interrupt 7 0: Disable external interrupt 7. 1: Enable interrupt request generated by the External Interrupt 7 input pin.
5 | EX6 | Enable External Interrupt 6 0: Disable external interrupt 6. 1: Enable interrupt request generated by the External Interrupt 6 input pin.
3 | EADC1 | Enable ADC1 End of Conversion Interrupt 0: Disable ADC1 End of Conversion interrupt. 1: Enable interrupt requests generated by the ADC1 End of Conversion Interrupt.
2 | ET4 | Enable Timer 4 Interrupt 0: Disable Timer 4 Interrupt. 1: Enable interrupt requests generated by TF4 (T4CON.7).
1 | EADC0 | Enable ADC0 End of Conversion Interrupt 0: Disable ADC0 End of Conversion interrupt. 1: Enable interrupt requests generated by the ADC0 End of Conversion Interrupt.
0 | ET3 | Enable Timer 3 Interrupt 0: Disable Timer 3 Interrupt. 1: Enable interrupt requests generated by TF3 (TMR3CN.7).
Set EIE2.0 (ET3) to 1 to enable interrupt requests by TF3 (Timer 3 overflow)
Each time the timer overflows, the ISR will be automatically executed
EIE2 |= 0x01; // Enable
// Timer 3
// Interrupt
// requests
Notes: <number>
<footer>
<header>
<date/time>
Set the bit ET3 (EIE2.0) to enable interrupts on Timer 3 overflow.

## Slide 25: Timer 2—16-Bit Auto-Reload Mode (Mode 1)
Reload value held in the capture registers (RCAP2L+RCAP2H or RCAP2)
Notes: <number>
<footer>
<header>
<date/time>
This functional block diagram shows the operation of Timer 2 in Mode 1 (16-bit auto-reload mode). T2 (TL2+TH2) is used as the 16-bit timer count register while the reload value is held in the Capture Registers (RCAP2L+RCAP2H or RCAP2).
T2M bit in register CKCON decides whether SYSCLK or SYSCLK/12 is used. When the timer is enabled (by setting TR2 to logic “1”), TCLK starts triggering the count register. When the count register overflows (going from FFFFh to 0000h), the timer overflow flag (TF2) will be set and the value in the reload register will be transferred to the count register. If the Timer 2 Overflow Interrupt has been enabled, then it will be generated and the corresponding ISR will be automatically executed.
Timer 2 may be triggered by an external source (T2) instead of SYSCLK. The crossbar will need to be programmed accordingly to make a pin available for T2 input.
In general, the rate at which the timer overflows can be controlled by changing the system clock frequency, choosing SYSCLK or SYSCLK/12, and choosing a different value for reload (in RCAP2).

## Slide 26: Timer 2: 16-Bit Auto-Reload Mode (Mode 1)
Programming Steps
  Step 1: Select the desired system clock frequency (CKCON)
  Step 2: Write the auto-reload value into the associated capture registers if using auto-reload mode (RCAP2L, RCAP2H)
  Step 3: Write the starting value for count up sequence into the associated count registers (TL2, TH2)
  Step 4: Select the mode (C/T2, CP/RL2), set the appropriate control bits (TR2) to turn on Timer (T2CON)
Notes: <number>
<footer>
<header>
<date/time>
By now you must have realised that the general approach to programming the timers is not much different from one timer to another. The operation of Timer 4 is exactly similar to Timer 2, albeit using different set of SFRs.

## Slide 27: T2CON—Timer 2 Control Register
Notes: <number>
<footer>
<header>
<date/time>
This table shows the various flags and control bits in the T2CON register. T4CON is the same.

## Slide 28: Mode Configuration for Timer 2
RCLK0 | TCLK0 | CP/RL2 | TR2 | Mode
0 | 0 | 1 | 1 | 16 Bit Counter/Timer with Capture
0 | 0 | 0 | 1 | 16 Bit Counter/Timer with Auto-reload
0 | 1 | X | 1 | Baud Rate Generator for UART0
1 | 0 | X | 1 | Baud Rate Generator for UART0
1 | 1 | X | 1 | Baud Rate Generator for UART0
X | X | X | 0 | Off
Notes: <number>
<footer>
<header>
<date/time>
The three modes of operation of Timer 2 (and also Timer 4) are 16-bit Counter/Timer with Capture, 16 Bit Counter/Timer with Auto-reload and Baud Rate Generator for UART0 (or UART1 for Timer 4). These are selected by programming the RCLK0, TCLK0, CP/RL2 and TR2 bits of the T2CON register for Timer 2. Fro Timer 4, the corresponding bits are RCLK1, TCLK1, CP/RL4 and TR4.

## Slide 29: Timer 2—Programming Example
//-- Configure Timer2 to auto-reload and generate an interrupt at interval
//-- specified by <counts> using SYSCLK/12 as its time base.
void Init_Timer2 (unsigned int counts)
{
CKCON = 0x00; // Define clock (T2M). Timer 2 // uses system clock DIV BY 12
// CKCON |= 0x20; if you want to use system clock
T2CON = 0x00;
// T2CON.1 = 0 --> T2 set for Timer function // (C/T2) i.e.incremented by clock defined by T2M
// T2CON.0 = 0 --> Allow Auto-reload on Timer2 overflow (CP/RL2)
// T2CON.3 = 0 --> High-to-Low transitions on // T2EX ignored (EXEN2)
// T2CON.2 = 0 --> Disable Timer2
RCAP2 = -counts; // Init reload values in the Capture registers
T2 = 0xFFFF; // count register set to reload
// immediately when the first clock occurs
IE |= 0x20; // IE.5, Enable Timer 2 interrupts (ET2)
T2CON |= 0x04; // Start Timer2 by setting TR2 (T2CON.2) to 1
}
Notes: <number>
<footer>
<header>
<date/time>
Programming example for setting up Timer 2 in auto-reload mode.

## Slide 30: Timer 2—16-Bit Counter/Timer with Capture (Mode 0)
Under this mode, the timer functions as a normal 16 bit timer, setting the TF2 bit upon a FFFFH to 0000H transition of the count registers
An interrupt is generated if it is enabled
The key difference is that a capture function can be enabled to load the current value of the count registers into the capture registers at the falling edge of T2EX
Notes: <number>
<footer>
<header>
<date/time>
In the Capture mode, the timer functions as a normal 16 bit timer, setting the timer overflow flag, TF2, upon a FFFFH to 0000H transition of the count register. An interrupt is generated if it is enabled. The key difference is that a capture function can be enabled to load the current value of the count registers into the capture registers.

## Slide 31: Timer 2—16-Bit Counter/Timer with Capture (Mode 0)
Notes: <number>
<footer>
<header>
<date/time>
This functional block explains the operation of Timer 2 in Mode 0 (16-Bit Counter/Timer with Capture).

## Slide 32: Timer 2—16-Bit Counter/Timer with Capture (Mode 0)
To enable the capture feature, the EXEN2 (T2CON.3) bit must be set to 1
A high-to-low transition on the T2EX input pin causes the following to occur:
  The 16-bit value in timer 2 count registers (TH2, TL2) is loaded into the capture registers (RCAP2H, RCAP2L)
  The timer 2 external flag (EXF2) is set to 1
  A timer 2 interrupt is generated if interrupt generation has been enabled
Notes: <number>
<footer>
<header>
<date/time>
This is how the capture function is accomplished –
First enable the capture feature, by setting EXEN2 (T2CON.3) bit to 1.
T2EX input has to be allocated a pin by programming the digital cross.
A high-to-low transition on the T2EX input pin causes the following to occur:
The 16-bit value in Timer 2 count registers (TH2, TL2) is loaded into the capture registers (RCAP2H, RCAP2L)
The Timer 2 External Flag (EXF2) is set to 1
A Timer 2 interrupt is generated if interrupt generation has been enabled

## Slide 33: www.silabs.com/MCU