## Slide 1: Lecture 6
Assembler Directives

## Slide 2: Assembler Directives
Code generation flow
Assembler directives—Introduction
Segment control
  Generic segment (SEGMENT, RSEG)
  Absolute segment (CSEG, DSEG and XSEG)
Address control
  ORG, USING, END
Symbol definition
  EQU, SET, CODE, DATA, IDATA, XDATA
Memory initialization/reservation
  DB, DW, DD, DS
Example program template
Notes: <number>
<footer>
<header>
<date/time>
In this lecture we will look at the various assembler directives. Assembler directives are special codes placed in the assembly language program to instruct the assembler to perform a particular task such as allocating memory for variables, changing register banks, defining symbols etc.

## Slide 3: Code Generation Flow
Assembly Code
Object Code
Assembler
C Code
Object Code
Linker
Machine Code
Compiler
Notes: <number>
<footer>
<header>
<date/time>
The diagram shows the code generation flow for both assembly and C languages. Note the linker is the same because it deals with object code.

## Slide 4: Assembler Directives—Introduction
Assembler Directives are not assembly language instructions as they do not generate any machine code
  They are special codes placed in the assembly language program to instruct the assembler to perform a particular task or function
  They can be used to define symbol values, reserve and initialize storage space for variables and control the placement of the program code
Assembler directives are typically specific to a particular assembler. We will be using the Keil A51 Assembler in this course.
The ASM directives are grouped into the following categories:
  Segment control
  Address control
  Symbol definition
  Memory initialization/reservation
Notes: <number>
<footer>
<header>
<date/time>
Assembler directives do not generate any machine code. There are four groups of assembler directives – Address Control, Symbol definition, Memory Reservation/Initialisation, and Segment Control.

## Slide 5: Segment Control
In x51 CPU structure, a contiguous block of code or data memory is usually referred to as a segment
  Examples:
    A function definition (code memory)
    An array (data memory)
There are two types of segments based on whether or not they are relocatable
  Generic or relocatable
  Absolute
Each of the two types of segments can be specified as one of five memory classes
  CODE, DATA, IDATA, XDATA, BDATA/BIT
Notes: <number>
<footer>
<header>
<date/time>
A segment is a block of code or data memory. There are two types of segments – generic and absolute.

## Slide 6: Generic (Relocatable) Segment
Generic segments are created using the SEGMENT directive
The final memory location for a generic segment is assigned by the linker
The format is as follows:
<Symbol > SEGMENT <segment_memory_class>
Example:
MYDATA SEGMENT DATA
The above directive defines a relocatable segment named as MYDATA, with a memory class of DATA
  Once the above segment name has been defined, the next step is to select that segment by using the RSEG directive as shown in the example below
RSEG MYDATA
Whenever the above statement is encountered, the MYDATA segment will become the current active segment until the assembler comes across another RSEG directive, which will then define another segment area
Notes: <number>
<footer>
<header>
<date/time>
A relocatable segment may be created using this directive.

## Slide 7: Absolute Segment
Absolute segment means a fixed memory segment. Absolute segments are created by CSEG, DSEG and XSEG directives.
The final location of the segment is known at compile time
The format of this directive is as follows:
CSEG AT <address> ; defines an absolute code segment
DSEG AT <address> ; defines an absolute data segment
XSEG AT <address> ; defines an absolute external data segment
Example:
CSEG AT 0300H ;select code segment and set ;the starting address at 0300H
DSEG AT 0400H ;select data segment and set ;the starting address at 0400H
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Address Control—ORG
The specified format for the ORG directive is:
ORG <expression>
The ORG directive is used to set the location counter in the current segment to an offset address specified by the expression
However, it does not alter the segment address. The segment address can only be changed by using the standard segment directives.
Example:
ORG 80H ;Set location counter to 80H
The ORG directive need not only be used in the code segment but can be used in other segments like the data segment as well.
For example, to reserve one byte memory space each at locations SECONDS and MINUTES in the data segment, we would write:
  DSEG ;data segment
  ORG 30H
  SECONDS: DS 1
  MINUTES: DS 1
Notes: <number>
<footer>
<header>
<date/time>
The ORG directive sets the location counter to a specified offset address within the current segment. It can be used in Code and Data segments.

## Slide 9: Address Control—END
The specified format for the directive is:
END
The END directive indicates the end of the source file
It informs the assembler where to stop assembling the program
  Hence any text that appears after the END directive will be ignored by the assembler
The END directive is required in every source file
  If it is not written at the end of the program, the assembler will generate an error message
Notes: <number>
<footer>
<header>
<date/time>
The END directive indicates the end of the source file and informs the assembler where to stop assembling the program. It is a must in every source file.

## Slide 10: Symbol Definition
The symbol definition directive assigns a symbolic name to an expression or a register
  This expression can be a constant number, an address reference or another symbolic name
Sometimes it is an advantage to use a symbol to represent a value or a register because it makes the program more meaningful to a user
Another advantage is, by equating the symbol to a value, the user only needs to change it once at the directive statement
  The rest of the statements that make a reference to the symbol will be updated automatically
Notes: <number>
<footer>
<header>
<date/time>
The symbol definition directive assigns a symbolic name to an expression or a register. Often done to make the program more meaningful to a user. Also helps in code maintenance/upgrade.

## Slide 11: Symbol Definition—EQU, SET
The format of the EQU and SET directives are as follows:
    Symbol EQU <expression>
    Symbol EQU <register>
    Symbol SET <expression>
    Symbol SET <register>
This is similar to the “#define” macro definition in C
expression can include simple mathematical operators like ‘+’, ’-‘, ‘ * ‘, ‘/’, MOD
register includes A, R0, R1, R2, R3, R4, R5, R6 and R7
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Symbol Definition—EQU, SET
Examples:
    COUNT EQU R3 ;equate to a register
    TOTAL EQU 200 ;equate to a constant
    AVERG SET TOTAL/5
    TABLE EQU 10
    VALUE SET TABLE*TABLE
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Symbol Definition—CODE, DATA, IDATA, XDATA
Each of these directives assigns an address value to a symbol. The format of the directive is as follows:
Symbol BIT <bit_address>
Symbol CODE <code_address>
Symbol DATA <data_address>
Symbol IDATA <idata_address>
Symbol XDATA <xdata_address>
bit_address The bit address which is available from bit-addressable location 00H through 7FH as an offset from byte location 20H
code_address The code address ranging from 0000H to 0FFFFH
data_address The address is from 00H to 7FH (internal data memory) and the special function register address from 80H to 0FFH
idata_address The address is ranging from 00H to 0FFH
xdata_address The external data space ranging from 0000H to 0FFFFH
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Symbol Definition—CODE, DATA, IDATA, XDATA
Example:
Act_bit BIT 2EH ;Use bit location 2EH ;as Act_bit
Port2 DATA A0H ;A special function ;register, P2
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Memory Initialization/Reservation
The directives for memory initialization and reservation are DB, DW and DD
These directives will initialize and reserve memory storage in the form of a byte, a word or a double word in code space
The directive to reserve memory without initialization is DS
This directive will reserve specified number of bytes in the current segment
Notes: <number>
<footer>
<header>
<date/time>
These directives will initialize or reserve memory space in the form of a byte, a word, or a double word in the code space.

## Slide 16: DB (Define Byte)
The DB directive initializes code memory with a byte value
The directive has the following format:
<label>: DB <expression>, <expression>, …
label
is the starting address where the byte values are stored
expression
is the byte value, it can be a character string, a symbol, or an 8-bit constant
Notes: <number>
<footer>
<header>
<date/time>
Initializes code memory with a byte value.

## Slide 17: DB (Define Byte)
Example:
CSEG AT 200H
MSG: DB ‘Please enter your password’, 0
ARRAY: DB 10H,20H,30H,40H,50H
The above string of characters will be stored as ASCII bytes starting from location 200H, which means location [200H]=50H, [201H]=6CH and so on
Notice that the DB directive can only be declared in a code segment
  If it is defined in a different segment, the assembler will generate an error
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: DW (Define Word)
The DW directive initializes the code memory with a double byte or a 16-bit word
The directive has the following format:
<label>: DW <expression>, <expression>, …
Example:
;2 words allocated
CNTVAL: DW 1025H, 2340H
;10 values of 1234H starting from location XLOC
XLOC: DW 10 DUP (1234H)
The DUP operator can be used to duplicate a sequence of memory contents
The DW directive can only be used in the code segment
  If it is defined in other segments, the assembler will give an error message
Notes: <number>
<footer>
<header>
<date/time>
Initializes code memory with a double-byte value (16-bit data).
The DUP operator can be used to duplicate a sequence of memory contents.

## Slide 19: DD (Define Double Word)
The DD directive initializes the code memory with double word or 32-bit data value
The directive has the following format:
<label>: DD <expression>, <expression>, …
Example:
ADDR: DD 820056EFH, 10203040H
EMPT: DD 3 DUP ( 0 )
Same as the DB and DW directives, DD can only be specified in the code segment
  If it is declared in other segment it risks having error message generated by the assembler
Notes: <number>
<footer>
<header>
<date/time>
Initializes code memory with a double-word value (32-bit data).

## Slide 20: DS (Define Storage)
The DS directive reserves a specified number of bytes in the current segment
It can only be used in the currently active segment like CSEG, ISEG, DSEG or XSEG
The DS directive has the following format:
<label>: DS <expression>
The expression can not contain forward references, relocatable symbols or external symbols
Notes: <number>
<footer>
<header>
<date/time>
Reserves a specified number of byte space in the memory in the currently active segment.

## Slide 21: DS (Define Storage)
Example:
XSEG AT 1000H ;select memory block from ;external memory, starting ;address from 1000H
Input: DS 16 ; reserve 16 bytes
Wavetyp: DS 1 ; reserve 1 byte
The location counter of the segment is incremented by one byte every time the DS statement is encountered in the program
The programmer should be aware that no more than 16 byte values should be entered starting from the address ‘Input’ as shown in the above example
Notice that the bytes are not initialized, just reserved
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Example Program Template
;-----------------------------------------------------------
$include (c8051f020.inc) ;Include register definition file
;-----------------------------------------------------------
; EQUATES
;-----------------------------------------------------------
CR EQU 0DH ;Set CR (carriage return) to 0DH
;-----------------------------------------------------------
; RESET and INTERRUPT VECTORS
;-----------------------------------------------------------
; Reset Vector
CSEG AT 0 ; Jump to the start of code at
LJMP Main ; the reset vector
; Timer 4 Overflow Vector
ORG 83h ; Jump to the start of code at
LJMP TIMER4INT ; the Timer4 Interrupt vector
;-----------------------------------------------------------
; DATA SEGMENT
;-----------------------------------------------------------
MYDATA SEGMENT DATA
RSEG MYDATA ; Switch to this data segment.
ORG 30h
Input: DS 16
temp: DS 1
Notes: <number>
<footer>
<header>
<date/time>
An assembly language program template is shown here.

## Slide 23: Example Program Template
;-----------------------------------------------------------
; CODE SEGMENT
;-----------------------------------------------------------
MYCODE SEGMENT CODE
RSEG MYCODE ; Switch to this code segment
USING 0 ; Specify register bank
; for main code.
Main: ; Insert Main Routine of program here
; … …
; … …
;-----------------------------------------------------------
; Timer 4 Interrupt Service Routine
;-----------------------------------------------------------
TIMER4INT: ; Insert Timer 4 ISR here
; … …
; … …
RETI
;-----------------------------------------------------------
; Global Constant
;-----------------------------------------------------------
Rdm_Num_Table:
DB 05eh, 0f0h, 051h, 0c9h, 0aeh, 020h, 087h, 080h
DB 092h, 01ch, 079h, 075h, 025h, 07ch, 02bh, 047h
;-----------------------------------------------------------
; End of file.
END
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: www.silabs.com/MCU