## Slide 1: Lecture 7
Programming the C8051F020
Using C Language

## Slide 2: Programming C8051F020 Using C Language
Code generation flow
Simple C program structure
Register definitions
16-bit SFR definitions
Summary of data types
Internal data memory
Bit-valued and bit-addressable data
External data memory
Operators—relational, logical, bit-wise, compound
Notes: <number>
<footer>
<header>
<date/time>
This lecture is NOT to teach C Programming as such, though we are going to quickly revise some standard things like the C operators, especially the bit-wise operators which are extensively used in embedded programming. We will look at things which are specific to this microcontroller, such as how to create a bit-valued and bit-addressable variable, or how to write an interrupt function etc.

## Slide 3: Code Generation Flow
Assembly Code
Object Code
Assembler
C Code
Object Code
Linker
Machine Code
Compiler
Notes: <number>
<footer>
<header>
<date/time>
The diagram shows the code generation flow for both assembly and C languages. Note the linker is the same because it deals with object code.

## Slide 4: Simple C Program Structure
//------------------------------------------------------------
// Basic blank C program that does nothing
// other than disable the watch dog timer
//------------------------------------------------------------
//------------------------------------------------------------
// Includes
//------------------------------------------------------------
#include <C8051F020_defs.h> // Include SFR declarations
void main (void)
{
EA = 0; // Disable global interrupts
WDTCN = 0xde; // Disable watchdog timer
WDTCN = 0xad;
EA = 1; // Enable global interrupts
while(1); // Stops the program from terminating and restarting
}
Notes: <number>
<footer>
<header>
<date/time>
This is an example of a C program with the header file included.
You must always indent your code as it goes a long way in making your program readable and legible.
Write generous comments (short of writing elaborate stories!!).

## Slide 5: Register Definitions
Register definitions must be made available to your program via the use of include files
The file C8051F020_defs.h contains all the definitions of the special function registers (SFRs) and the bit registers
Example:
sfr P0=0x80; // Port 0
sfr SBUF0=0x99; // Serial Port 0 Buffer
sfr IE=0xA8; // Interrupt Enable
sfr WDTCN=0xFF; // Watchdog Timer Control
sbit EA=IE^7; // Global Interrupt enable
Notes: <number>
<footer>
<header>
<date/time>
The header file c8051f020_defs.h contains all the definitions of the 8-bit Special Function Registers (SFRs) and the bit registers. It also contains 16-bit SFR definitions. It must be included in your program.

## Slide 6: 16-Bit SFR Definitions
Many of the newer 8051 derivatives, like C8051F020, use two SFRs with consecutive addresses to specify 16-bit values
The include file C8051F020_defs.h contains the 16-bit SFR definitions as well
Since none of the 16-bit SFR addresses end with 0H or 8H, they are NOT bit-addressable
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: C Language—Summary of Data Types
Data Type | Bits | Bytes | Value Range
signed char | 8 | 1 | -128 to +127
unsigned char | 8 | 1 | 0 to 255
enum | 8/16 | 1 or 2 | -128 to +127 or -32768 to +32767
signed short | 16 | 2 | -32768 to +32767
unsigned short | 16 | 2 | 0 to 65535
signed int | 16 | 2 | -32768 to +32767
unsigned int | 16 | 2 | 0 to 65535
signed long | 32 | 4 | -2147483648 to 2147483647
unsigned long | 32 | 4 | 0 to 4294967295
float | 32 | 4 | ±1.175494E-38 to ±3.402823E+38
bit | 1 | - | 0 to 1
sbit | 1 | - | 0 to 1
sfr | 8 | 1 | 0 to 255
sfr16 | 16 | 2 | 0 to 65535
8051 Compiler Specific
ANSI C
Some compilers use 4 bytes for these
Notes: <number>
<footer>
<header>
<date/time>
This table shows the summary of the various data types, their sizes and the range of values that can be stored in them. Please note that the Keil C51 compiler that is bundled with the SiLabs development board does not support floating point operations.

## Slide 8: Internal Data Memory
Review
  Up to 256 bytes of internal data memory are available
  The first 128 bytes of internal data memory are both directly addressable and indirectly addressable
  The upper 128 bytes of data memory (from 0x80 to 0xFF) can be addressed only indirectly
  There is also a 16 byte area starting at 20h that is bit-addressable
Access to internal data memory is very fast because it can be accessed using an 8-bit address.
  Internal data memory is limited to a maximum of 256 bytes (28 = 256)
In C, a declared variable can be explicitly placed in a certain area of memory. If no memory specifier is used, the compiler puts the variable in the memory space associated with the chosen memory model.
  Example: int ADC_Result;
    SMALL memory model: this variable is placed in DATA space
    COMPACT memory model: this variable is placed in IDATA space
    LARGE memory model: this variable is placed in XDATA space
Notes: <number>
<footer>
<header>
<date/time>
Access to internal data memory is very fast because it can be accessed using an 8-bit address. Hence variables that are very frequently used in a program should be stored in the internal memory to improve the program efficiency. The bit-addressable memory space is rather limited – only 16 bytes.

## Slide 9: Internal Data Memory
Internal data can be broken down into three distinct data types: data, idata and bdata
The data memory specifier always refers to the first 128 bytes of internal data memory. Variables stored here are accessed using direct addressing (default for SMALL memory model).
The idata memory specifier refers to all 256 bytes of internal data memory
  This memory type specifier code is generated by indirect addressing, which is slightly slower than direct addressing
The bdata memory specifier refers to the 16 bytes of bit-addressable memory in the internal data area (20h to 2Fh)
  This memory type specifier allows you to declare data types that can also be accessed at the bit level
Examples:
unsigned char data name;
int idata count;
int bdata status;
Notes: <number>
<footer>
<header>
<date/time>
There are three programming memory models to choose from – SMALL, COMPACT and LARGE. The memory model required is selected using the #pragma compiler control directive. In the SMALL memory model the default storage location is the lower 128 bytes of internal memory while in the LARGE memory model the default storage location is the externally addressed memory. The choice of which memory model to use depends on the program, the anticipated stack size and the size of data. If the stack and the data cannot fit in the 128 bytes of internal memory then the default memory model should be LARGE, otherwise SMALL should be used.
The variables may be specified to be data, idata or bdata. Direct addressing is faster that indirect addressing.

## Slide 10: Bit-Valued and Bit-Addressable Data
Bit-valued data and bit-addressable data are stored in the bit-addressable memory space (address 0x20 to 0x2F)
They are declared using the bdata, bit or sbit memory specifiers
Example:
The integer variable X declared above is bit-addressable (individual bits of this variable can be accessed)
The variable flag may be used to store only a one-bit value, effectively 0 or 1
int bdata X; // 16-bit bit-addressable variable X
bit flag; // bit-valued variable flag
Notes: <number>
<footer>
<header>
<date/time>
Bit-valued data and bit-addressable data are stored in the bit-addressable memory space. A bit-valued variable can store only a 1-bit data (either a value 0 or 1). Individual bits of a bit-addressable variable can be accessed.

## Slide 11: Bit-Valued and Bit-Addressable Data
The sbit data type is used to declare variables that access a particular bit field of a SFR or of a previously declared bit-addressable variable
Example:
sbit variable cannot be declared local to a function. It must be a global variable.
X7_Flag is a 1-bit variable that references bit number 7 of the bit-addressable integer variable X
Red_LED refers to bit number 1 of the bit-addressable port SFR P0
sbit X7_Flag = X^7; // bit 7 of X (bit variable)
sbit Red_LED = P0^1; // bit 1 of Port P0 (bit-addressable SFR)
Notes: <number>
<footer>
<header>
<date/time>
A sbit variable must be initialized to access a particular bit field of a SFR or of a previously declared bit-addressable variable.
More examples of sbit data declaration are-
sbit LED = P1^6;  The 1-bit variable LED refers to bit 6 of SFR P1
sbit SW2 = P3^7;  The 1-bit variable SW2 refers to bit 7 of SFR P3
The ^ operator is used to access a particular bit of a variable (SFR or bit-addressable variable).
sbit variable cannot be declared local to a function. It must be a global variable.

## Slide 12: Bit-Valued and Bit-Addressable Data
Another example:
You cannot declare a bit pointer or an array of bits
The bit valued data segment is 16 bytes or 128 bits in size, so this limits the amount of bit-valued data that a program can use
int bdata status;
bit s2 = status^5;
Notes: <number>
<footer>
<header>
<date/time>
In this example, the bit variable s2 is assigned the value of bit 5 of the bit-addressable variable status.
You cannot declare a bit pointer or an array of bits.

## Slide 13: External Data Memory
External data memory, up to 64 kB, can be read from and written to and is physically located externally from the CPU
Access to external data in XDATA space is very slow when compared to access to internal data
  This is because external data memory is accessed indirectly through the data pointer register (DPTR) which must be loaded with a 16-bit address before accessing the external memory
There are two different data types in Cx51 used to access external data: xdata and pdata
  The xdata memory specifier refers to any location in the 64 kB address space of external data memory (default for LARGE memory model)
  The pdata memory type specifier refers to only 1 page or 256 bytes of external data memory (default for COMPACT memory model)
    The pdata area is accessed using registers R0 and R1 indirectly (@R0 or @R1) instead of the DPTR (@DPTR), so accessing pdata is slightly faster than xdata. This is also what limits pdata to 256 bytes (R0 and R1 are 8 bits).
Notes: <number>
<footer>
<header>
<date/time>
Access to external data is very slow when compared to access to internal data. This is because external data memory is accessed indirectly using the data pointer (DPTR) register which must be loaded with a 16-bit address before accessing the external memory.
To access external data, you specify them to be either xdata or pdata.

## Slide 14: Arithmetic Operators
Arithmetic operators perform basic arithmetic operations
All arithmetic operators except the negation (–) operator have two operands.
Operator | Description
+ | Add
– | Subtract
* | Multiply
/ | Divide
% | Modulo (remainder of division)
– | Negation (unary minus)
unsigned int count = 0x0F;
// TMR2RL gets 0xFFFF-0x0F+1 = 0xFFF1
TMR2RL = -count;
The negation (unary minus) operator returns the 2’s complement value of the operand
  This is especially useful to specify a count that will be counted up rather than counted down
  Example:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Relational Operators
Relational operators compare data and the outcome is either True or False
if statements, for loops and while loops often make use of relational operators
Operator | Description
== | Equal to
!= | Not Equal to
< | Less than
> | Greater than
<= | Less than or equal to
>= | Greater than or equal to
Notes: <number>
<footer>
<header>
<date/time>
Relational operators compare data and the outcome of the operation is a Boolean value (i.e. True or False)

## Slide 16: Logical Operators
Logical operators operate on Boolean data (True and False values) and the outcome is also Boolean
Operator | Description
&& | Logical AND
¦¦ | Logical OR
! | Logical NOT
Notes: <number>
<footer>
<header>
<date/time>
Logical operators operate on Boolean data (True and False values) and the outcome is also Boolean.

## Slide 17: Bitwise Operators
The C language also has several bitwise operators
Bitwise operators affect a variable on a bit-by-bit basis
Example:
Result = Value1 & Value2;
  If Value1 = 00100100b and Value2 = 10100000b, the result of Value1 & Value2 is:
00100100b & 10100000b = 00100000b
Operator | Description
& | Bitwise AND
¦ | Bitwise OR
~ | Bitwise NOT (1’s Compliment)
^ | Bitwise Exclusive OR
<< | Shift Left
>> | Shift Right
Notes: <number>
<footer>
<header>
<date/time>
The bitwise operators are extensively used in embedded programming. These operators can manipulate data at the individual bit level.

## Slide 18: Usage of Bitwise Operators
Turning Bits On
  Turn on a particular bit by ORing with a 1
Turning Bits Off
  Turn off a particular bit by ANDing with a 0
Toggling Bits
  Turning a bit from off to on or on to off by EXCLUSIVELY ORing with a 1
Notes: <number>
<footer>
<header>
<date/time>
This slide shows you the typical use of various bitwise operators, such as ORing with a 1 to turn bits on, ANDing with a 0 to turn bits off and XORing with a 1 to toggle bits.
These operators are also used to check the status of a bit, whether it is 1 or 0.

## Slide 19: Checking the Status of a Bit
1
0
0
1
0
1
1
0
flags (variable)
0
0
0
0
0
0
1
0
MASK (constant)
0
0
0
0
0
0
1
0
flags & MASK
1
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
if ( (flags & MASK) == 0 )
printf(“flags.1 is OFF”);
else
printf(“flags.1 is ON”);
flags.1 is ON
flags.1 is OFF
Notes: <number>
<footer>
<header>
<date/time>
To check the status of a bit in flags, load a 1 in the corresponding bit position in mask.

## Slide 20: Shifting Data
The bitwise shift operators shift bits to the left or right
1
0
0
1
0
1
1
0
LEFT
RIGHT
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Left (<<) and Right Shift (>>)
1
0
0
0
1
0
1
0
LEFT
1
0
0
0
1
0
1
0
0
1
0
0
0
1
0
1
0
RIGHT
1
0
0
0
1
0
1
0
0
Notes: <number>
<footer>
<header>
<date/time>
This slide has animation showing the shifting numbers. Shifting data to the left by N positions multiplies it by 2N
Shifting data to the right by N positions divides it by 2N
This is a fast way of dividing numbers.

## Slide 22: Compound Arithmetic Operators
Operator | Description | Example | Equivalent
+= | Add to variable | X += 2 | X=X+2
-= | Subtract from variable | X -= 1 | X=X-1
/= | Divide variable | X /= 2 | X=X/2
*= | Multiply variable | X *= 4 | X=X*4
Notes: <number>
<footer>
<header>
<date/time>
Operators, such as arithmetic and bitwise logical, may be combined with assignment operator to create a compound operator.
X += 2;  read as “X is increased by 2”
X -= 1;  read as “X is decreased by 1” X /= 2;  read as “X is divided by 2”
X *= 4;  read as “X is multiplied by 2”

## Slide 23: Compound Bitwise Operators
Operator | Description | Example | Equivalent
&= | Bitwise AND with variable | X &= 0x00FF | X = X & 0x00FF
¦= | Bitwise OR with variable | X ¦= 0x0080 | X = X ¦ 0x0080
^= | Bitwise XOR with variable | X ^= 0x07A0 | X = X ^ 0x07A0
//-- Enable P1.6 as push-pull output
P1MDOUT |= 0x40;
//-- wait till XTLVLD pin is set
while ( !(OSCXCN & 0x80) );
C language also provides shortcut bitwise operators acting on a single variable (similar to the +=, -=, /= and *= operators)
Notes: <number>
<footer>
<header>
<date/time>
P1MDOUT |= 0x40;  Read as “ P1MDOUT is bitwise ORed with 0x40
This is same as P1MDOUT = P1MDOUT | 0x40;

## Slide 24: www.silabs.com/MCU