## Slide 1: Lecture 3
Silicon Labs ToolStick
Development Platform

## Slide 2: Contents
Microcontroller development systems
ToolStick overview
ToolStick base adapter
ToolStick MCUniversity daughter card
Using the ToolStick development platform
Software development tools
ToolStick MCUniversity daughter card demonstration

## Slide 3: Microcontroller Development Systems
Microcontroller development Systems typically consist of both hardware and software that are necessary to evaluate and develop code on a microcontroller
The hardware typically includes
  A target board that includes the MCU to be evaluated
  A means to program the microcontroller
  A means to debug the microcontroller while it is executing code
The software typically includes
  An integrated development environment (IDE)
    Assembler, compiler, linker and debugger
    Software to download the code to the microcontroller

## Slide 4: Microcontroller Development Systems
Example: Silicon Labs C8051F020-DK Development Kit
Kit Contents
  Software
    Silicon Labs integrated development environment (IDE)
    Evaluation Keil C51 tool chain (assembler, linker, and 4 Kb C-compiler)
    Source code examples and register definition files
    Documentation
  Hardware
    Target/prototyping PCB
    Wall power supply
    USB debug adapter
    USB cable

## Slide 5: ToolStick Overview
The ToolStick development platform provides a powerful development platform at a low cost
The ToolStick includes all necessary hardware in a USB stick
  USB debug adapter (BA—base adapter)
  Target MCU (DC—daughter card)
Development on the ToolStick platform can be done using software development tools available from Silicon Labs
  Integrated development environment (IDE)
  Virtual display tools

## Slide 6: ToolStick Development Platform
ToolStick Base Adapter
USB Debug Interface to PC
Can communicate with any Silicon Labs MCU
ToolStick MCUniversity Daughter Card
Development platform for C8051F020 MCU

## Slide 7: ToolStick Base Adapter Block Diagram

## Slide 8: ToolStick Base Adapter Hardware Overview
Silicon Laboratories MCU
Performs USB debug adapter and PC communication functions
Run/Stop LEDs
Indicate if target MCU is running or halted
Socket Connector
Accepts a 14-pin card-edge connector
Power LED
Indicates USB Bus power

## Slide 9: ToolStick Base Adapter Functionality
Provides a USB Debug interface to a Windows PC
Provides a UART Interface with optional hardware handshaking
  HID interface; no USB drivers need to be installed on PC
  Cannot be used simultaneously with the debug interface
Two multifunction pins
  GPIO pins that can be read or written from the PC OR
  Two UART handshaking pins (RTS and CTS)

## Slide 10: ToolStick UniDC Hardware Overview
I/O Pins
P0[7..2], P1, P2
Potentiometer
Linear output that sweeps from 0V to 3.3V
Target MCU C8051F020
Power LED
Indicates 3.3V is available
Reset Switch
Analog I/O Pins
Push-button Switches
P5[3..0]
LEDs
P5[7..4]
DIP Switches P4
Crystal
22.1184 MHz
Prototype Area

## Slide 11: Handling The ToolStick
Caution: The modular ToolStick components are not encased in plastic. This makes both the base adapter (BA) and the daughter cards (DC) susceptible to electrostatic discharge (ESD) damage.
Follow these recommendations to protect the hardware
  Never connect or disconnect a ToolStick daughter card from the base adapter while connected to a PC
  Always connect or disconnect a ToolStick by holding the large plastic connector or the edges of the boards
  Be careful when using the mechanical components, such as the potentiometers, so as to not stress the connectors

## Slide 12: Handling The ToolStick
The Wrong way to hold the ToolStick

## Slide 13: Handling The ToolStick
The Correct way to hold the ToolStick

## Slide 14: Connecting the ToolStick
Can connect the ToolStick directly to the PC
Can connect the ToolStick using the USB extension cable

## Slide 15: Software Development Tools
Silicon Laboratories IDE (integrated development environment)
  Connects to target device via debug adapter
  Allows programming and debugging of target MCUs
  Integrates third-party compilers
    Keil, SDCC, IAR, etc.
Silicon Labs IDE Screen Shot

## Slide 16: Software Development Tools
Virtual Tools
  ToolStick terminal
  Virtual LCD
  Virtual oscilloscope

## Slide 17: ToolStick UniDC Demonstration
Step 1: the firmware disables a peripheral called the watchdog timer
Step 2: the firmware configures a port pin to output mode
Step 3: the device lights up an LED connected to that port pin
Step 4: the firmware enters an infinite loop
Notes: We will learn about the watchdog timer in a later lecture.

## Slide 18: Installing the IDE and Demo Programs
Download the ToolStick University Kit package from:
http://www.silabs.com/MCUniversity
Install the ToolStick University Kit package and IDE to the same directory:
c:\Silabs\MCU
Insert the ToolStick into a USB port on the PC once installation is complete

## Slide 19: Opening the Demo Project
Launch the IDE once the installation is complete
Open the project from the Project menu
Browse to C:\SiLabs\MCU\ToolStick\UniversityDC\Firmware\SimpleDemo\
Open “UniDC_SimpleDemo.wsp”
Notes: The Silicon Labs IDE has native support for many compilers.
Go to the Project -> Tool Chain Integration menu and use the drop-down menu to see the toolsets supported by the IDE.

## Slide 20: Building the Demo Project
Build the project from the Project menu
Building the project creates an object file that can be downloaded to the device
Notes: When the project is built, the output window of the IDE will show this warning:
*******************************************************************************
RESTRICTED VERSION WITH 1000H BYTE CODE SIZE LIMIT; USED: 00F5H BYTE ( 5%) *******************************************************************************
This is because the ToolStick CD comes with a Demo version of the Keil toolset. This demo version has two restrictions:
A 2K code size limit
No floating point library
To get rid of the restrictions, the customer will need to upgrade to a full version of Keil.

## Slide 21: Configuring Connection Options
Configure the “Connection Options” under the Options menu
Select USB debug adapter as the adapter interface
  The Adapter selection drop-down box will display a serial number like the one shown
Select “JTAG” for the debug interface
Notes: “The JTAG interface is a industry-standard interface used to program and debug devices. It uses four signals and ground”
If the “USB Debug Adapter” selection is not available, make sure that the ToolStick is properly plugged into the USB port. You might have a wait for a few seconds after plugging in for the first time to allow Windows to install the device driver for the device.

## Slide 22: Connecting and Downloading Firmware
Click on the Connect button to connect the IDE to the demo board
Once the IDE is connected, click on the Download button to download the firmware to the device

## Slide 23: Running and Stopping the Microcontroller
Click on the green Go button to start executing firmware on the demo board
Notice a green LED light up on the ToolStick MCUniversity daughter card
When the device is running, it can be stopped using the red Stop button
The LED will hold its current state when the processor is halted

## Slide 24: Opening the Ports Debug Window
Halt the processor by clicking on the Stop button
Open the Ports SFR View using the View → Debug Windows → SFR’s → Ports menu option
Notes: All registers on the device can be viewed and modified when the device is in a halt state. The registers are grouped together in the SFR debug windows according to which peripheral or part of hardware they belong.

## Slide 25: The Ports Debug Window
The ADC Debug Window shows the values of the SFR registers when the processor is halted
The values in red are the values that have changed since the last halt
This window can be used to change SFRs without recompiling
Bit 4 of P5 indicates that LED D1 is switched on
Notes: In this picture, the value of the P5 register is red in the picture because the value has changed since the last time the device was halted. This feature is useful for informing the user which registers/memory locations are changing while debugging.

## Slide 26: Changing the Port Latch Value
The Port pin can be configured in “real-time”
In the Ports Debug Window, change the P5 value to 0x0F
Then click the Refresh button to write the new value to the register
Observe the P5.4 LED (D1) has now turned off
Key point: The IDE has full access to the hardware allowing registers to be changed in real-time

## Slide 27: Using the Watch Window
Halt the processor using the Stop button
In the code editor window, right-click on the variable name count and select “Add count to Watch → Default”
The variable will be added to a watch window and its value will be updated every time the processor is halted
Key point: The watch window makes debugging faster and easier because you can see any memory location in RAM, XRAM, or CODE in one window
Notes: The “count” variable does not have any useful purpose in this code. This has been added just to demonstrate the features of the IDE.

## Slide 28: Using the Watch Window
Alternately start and stop the processor using the “Go” and “Stop” buttons
Notice that the count variable increments as the MCU executes code
The value of the variable can also be changed directly from the Watch Window when the device is in a halted state

## Slide 29: Setting a Breakpoint
Stop the processor by using the Stop button
Right-click on the variable name count and select “Insert/Remove Breakpoint”
A hardware breakpoint is set on the device
The editor window shows the location of breakpoints using a red dot beside the line of code

## Slide 30: Debugging with a Breakpoint
Once the breakpoint is set, click “Go” to continue program execution
The device will halt once the program reaches a hardware breakpoint
Click “Go” a few times to watch the variable increment
Key point: Breakpoints allow the developer to easily run to a section of code that needs debugging and no CPU resources are wasted because they are fully implemented in hardware
Notes: Breakpoints can be placed on any instruction.

## Slide 31: Single-Stepping Through the Firmware
Using the IDE, the firmware can be executed one assembly instruction at a time using the Single-Step function
Click the Disassembly Button to open the Disassembly Window
Once the device is halted, click the Single-Step Button and watch the device execute one assembly instruction each time
Notes: “In many situations, debugging the C source code is not sufficient. You need to know exactly how the compiler translated a C instruction. The disassembly window and the single-step functions provide the ability to run one assembly instruction at a time and monitor its output”

## Slide 32: Additional Resources
Refer to the following User’s Guides
  ToolStickUniDC User’s Guide
  AN333: ToolStick Virtual Tools User’s Guide
  Located at these default locations:
    C:\SiLabs\MCU\ToolStick\UniversityDC\Documentation\
    C:\SiLabs\MCU\ToolStick\Documentation\
Refer to the following additional examples
  UniDC_FeaturesDemo
  UniDC_VirtualTools_Demo
  Located at this default location:
    C:\SiLabs\MCU\ToolStick\UniversityDC\Firmware

## Slide 33: www.silabs.com/MCU